## Slide 1
Phase 6 Nutrient Management Expert Panel deliberations & progress
February 24, 2016
Historical base-line conditions (i.e.1985) are used as uniform reference point for non-nutrient management conditions at the field scale.
The concept of “negative efficiency” for non-nutrient management acres is eliminated.
The previously proposed “Core Nutrient Management” base-line threshold, or “neutral” condition, is eliminated.
Core Nutrient Management BMP becomes an efficiency in the models.
Supplemental Nutrient Management BMP efficiencies are additive to Core Nutrient Management BMP efficiencies, but do not exist without Core BMPs.
Nutrient Management BMPs can represent adjusted rate of nutrient application through application of an efficiency factor applied to the base rate.

## Slide 2
No credit
for nutrient
management
Core Nutrient Management BMP (ALL core elements required to be implemented and verified)
N & P rate, timing and placement according to LGU recommendations at field level
P soil tests at field level
Manure analysis and volume - test value or book value
Spreader/applicator calibration
Yield estimates and cropping plan at field level
Cropping and manure history at field level
NO
YES
Credit for Core
Nutrient Management
BMP efficiency applied
Advanced N Assessment
PSNT
Manure analysis < 3 years old
On-farm replicated research
CSNT
N-loss risk assessments & models - Ammonia loss
Yield mapping
ISNT
On-farm strip trials
N-loss risk assessments & models - Leaching loss
FSNT
N-loss risk assessments & models - Denitrification losses
Whole farm balances
In-season sensors/remote sensing in general
Geo-spatial mapping
Advanced P Assessment
Soil test P remediation/declining
Soil tests < 3 years old
P Index assessment
Grid soil sampling
Manure analysis < 3 years old
On-farm replicated research
Yield mapping
On-farm strip trials
Whole farm balances
Geo-spatial mapping
If Core Nutrient Management BMP efficiency is applied, follow with advanced assessment for Supplemental Nutrient Management BMPs
N Rate Adjustment (implementation of one or more BMPs required)
N rate less than LGU recommendations
Split N applications
Variable rate N application
N Placement Adjustment (implementation of one or more BMPs required)
Subsurface injection or incorporation of applied N
N application setbacks from water
N Timing Adjustment (implementation of one or more BMPs required)
Split N applications
P Rate Adjustment (implementation of one or more BMPs required)
P-based manure rate based on crop P removal
P rate less than LGU recommendations
Variable rate P
Split P applications
P Placement Adjustment (implementation of one or more BMPs required)
Subsurface injection or incorporation of applied P
P application setbacks from water
P Timing Adjustment (implementation of one or more BMPs required)
P application in lower P-loss risk season
IMPLEMENTATION
IMPLEMENTATION
IMPLEMENTATION
IMPLEMENTATION
IMPLEMENTATION
IMPLEMENTATION
BMP Efficiency = 99%
BMP Efficiency = 99%
BMP Efficiency = 99%
BMP Efficiency = 99%
BMP Efficiency = 99%
BMP Efficiency = 99%
BMP Efficiency = 99%
All BMP efficiencies of 99% are fake