## Slide 1: A Overview of Stormwater Management in Maryland by Andrew T. Der, C.E.P.
Presentation for
the Citizen’s Advisory Committee to the
Chesapeake Executive Council
Baltimore, Maryland
Wednesday May 22, 2019

## Slide 2
What We Will Learn
How the Clean Water Act (CWA) is a basis for many of our current regulatory criteria
How the CWA regulates water resources and stormwater at the site level
How Maryland and localities apply stormwater management (SWM) criteria to new activities
How Maryland and localities apply stormwater management criteria to existing built lands

## Slide 3
Stormwater Management (SWM) and the Clean Water Act (CWA)

## Slide 4: What is the CWA?
1948 Federal Water Pollution Control Act and 1972 amendments
Most influential water law in history
Prohibits “discharges” for first time
Catalyst for other state and local programs we have today

## Slide 5: CWA Regulation
Establishes the means to regulate discharges into the Waters of the U. S. (WUS)
Rules under debate now – and also affect SWM – why?
U. S. EPA through the Maryland Department of the Environment (MDE) implements point source discharges/pollution controls
Gradually transitioned to also nonpoint source control – and farther upstream – this is key

## Slide 6: CWA Section 404
Regulates discharges to WUS, including wetlands, at the site level
Requires a U. S. Army Corps of Engineers (COE) and MDE permit
SWM, TMDL restoration projects need this permit also

## Slide 7: CWA Section 401 (aka WQC)
A Water Quality Certification must go with a Section 404 permit or FERC license
Requires the applicable state (MDE) to issue a WQC
401 WQC certifies that a 404 permit will not violate state water quality standards
This was also the first means to require true SWM in past
A sleeping giant - gives MDE a state veto

## Slide 8: CWA Section 401 in the Past
401 WQC conveys numerical and narrative water quality standards including EPA Anti-degradation Policy (ADP)
The ADP standard requires methods: “…to accomplish the objective of maintaining existing water quality…nonpoint sources shall achieve all cost effective and reasonable best management practices for nonpoint source control…”
First SWM but only when a 404 permit

## Slide 9: CWA Section 401 in the Present
What happened to the WQC?
It’s still there – now part of the joint COE/MDE tidal/nontidal wetland and waterway permit
SWM now accomplished by Section 402 NPDES, State SWM law, Forest Conservation Act (and Bay Critical Areas)
Except for (cue dramatic music) Conowingo Dam
Section 401 is the only regulatory control the state has

## Slide 10: CWA Section 402 (aka NPDES)
This is the big one for SWM
Referred to as National Pollutant Discharge Elimination System
Originally permitted individual point sources and industrial discharges – and still does
Over time, acknowledged stormwater discharges need regulation after NURP studies
But how could all stormwater discharges be regulated realistically?

## Slide 11: CWA Section 402 Synopsis
Administered by MDE programmatic permits in two phases every five years
Phase I authorizes new construction discharge via a Construction General Permit (GP) - and existing built stormwater systems by a Municipal Separate Storm Sewer System (MS4) General Permit
Phase II authorizes smaller disturbance thresholds for new construction discharges - and smaller MS4 localities and entities (MDTA, WSSC, WMATA
Some rural regions of Maryland (gray) not regulated and state-only SWM (or ag management) criteria applies

## Slide 12: Clean Water Act Section 303 (aka TMDL)
After the state lists their impaired waters, a Total Maximum Daily Load establishes the maximum pollutant level for restoring water
Been around for smaller segments – the Bay TMDL switches reference to include entire watershed - largest in the country (Conowingo newest)
MS4 compliance is a means for TMDL compliance through 3 Phases of Watershed Implementation Plans (WIP)
Non-MS4 jurisdictions have other challenges

## Slide 13
SWM at the State and Local Level – Getting it On the Ground

## Slide 14
New Construction and Stormwater

## Slide 15: How is SWM Applied at State Level?
Maryland’s SWM programs integrate ecological and resource with engineering criteria in context of limits of waters, including wetlands
MDE administers the CWA Sec 402 NPDES Construction General Permit criteria concurrently with local SWM ordinance
Compliance is achieved by a Stormwater Pollution Prevention Plan (SWPPP) but in Maryland not usually required if an approved MDE SWM plan - may still apply to industrial activities
Certain DoD and federal facilities may have own SWM mandate

## Slide 16: How is SWM Applied Locally?
Maryland applies own state SWM standards – triggered by - land - rather than WUS disturbance
Federal and state property regulated directly by MDE SWM, DNR Forest Conservation, and Bay Critical Area Commission
MDE SWM Law delegated to localities and administered by local ordinance
Forest Conservation Act delegated to localities and administer waters buffers by local ordinance
In Critical Area, waters buffers, impervious limits, and IDA SWM overlay administered by local planning criteria

## Slide 17: What is Maryland’s SWM Law?
2012 Maryland Erosion and Sediment Control Law - temporary conditions – incorporates E/S Manual
2007 Maryland Stormwater Management Act – permanent conditions - incorporates Maryland Stormwater Design Manual for BMPs
  Formalizes Environmental Site Design (ESD) to the Maximum Extent Practicable (MEP) – to maintain channel stability and mimic “woods in good condition” to receiving waters
  Structural stormwater practices may be used if determined to be necessary
  BMPs updated as applicable by CBP Expert Panels assisted by Chesapeake Stormwater Network and WQGIT

## Slide 18: Best Management Practices
BMPs are not just structural
Early Planning
Environmental site design
Maximize stream buffer and sheet flow - disconnect impervious surfaces
Re-development criteria
Urban redevelopment of legacy land and unmanaged stormwater done under criteria requires retrofit of existing unmanaged runoff as well as offsite runoff – and can be net gain and contribute to MS4 goals

## Slide 19: Structural BMP Synopsis
Smaller Volumes - try first
“First Flush” is preferred and most
compatible with ESD at-source
and/or pretreatment quality control
Infiltration
  trench/basin
Filtering
  sand filter/bioretention
Hydrodynamic Devices above or underground
  Curb & gutter vortex/filter basin
“Newer” Technology
  pervious surfaces/green roofs
Larger Volumes – if needed
When preferred is Insufficient
for quantity and quality
Stormwater Ponds
  wet pond
  wet ED pond
  dry ED pond (for cold water w/
  pre-treatment)
  multiple pond system
Stormwater Wetlands
  shallow marsh
  ED shallow wetland
  pond/wetland systems
Notes: <number>
The stormwater treatment practices presented in this slide show fall into five major categories: stormwater ponds, stormwater wetlands, infiltration practices, filtering practices, and open channels. Within each category, there are several design variations.

## Slide 20
Developed Urban Areas and pre-existing Stormwater – Our Biggest Challenge

## Slide 21: How is SWM Applied?
Phase I and Phase II NPDES MS4 Permits - only permitting to “clean up the past” - how can existing unmanaged stormwater be managed?
Fundamental MS4 permit requirements:
• Identify stormwater/pollutant sources – biggest regulatory GIS mandate ever
• Map stormwater infrastructure, outfalls, BMPs with drainage areas
• Map impervious surfaces, water quality monitoring, improvement projects
• Maintain an E/S Control and SWM Program
• Implement an Illicit Discharge Detection and Elimination enforcement program
• Identify sources of litter and floatables and implement education program
• Public education and outreach – a means for existing non-managed areas – can be a means for CAC Land Use and Urban Stormwater Subcommittee

## Slide 22: Additional MS4 Compliance
More substantial MS4 SWM commitments
Uses the reporting information to supplement WIPs - untreated impervious GIS acreage becomes the baseline impervious from which restoration is measured
By the end of the five year permit term, complete 20% restoration of the baseline impervious area that has not already been restored to the MEP – most formidable
This is how Maryland has committed to EPA to address the Bay TMDL WIP – other Bay states rely on BMPs alone
Each treated acre is one “imperious acre credit” and must be tracked with an annual report to MDE per MDE stormwater wasteload allocation guidance

## Slide 23: Alternative MS4 BMP Strategies
Permittees can use a variety of offsets for built environments
Street sweeping
Reforestation/tree planting
Removing impervious
End-of-pipe step pool storm conveyance and outfall stabilization
Catch basin cleaning
Stormdrain vacuuming
Shoreline management
Septic upgrades
Stream restoration – big one – is it too big?
Compliance with new 2018 MDE water quality trading regulations - Anne Arundel and Baltimore Counties already requested modification to their NPDES MS4 permit 20% impervious reduction requirements as a compliance option

## Slide 24: Will MS4 Compliance be Achieved?
Are counties meeting MS4 permit goals?
Will compliance be desktop-based?
Many MS4s having difficulty – and compliance can be trading credits from wastewater programs
Likely: Anne Arundel County and SHA - expects to meet goal
Maybe/yes: Baltimore City - proposing trash and street sweeping
Maybe: Frederick County - may be close
No: Montgomery County is under Consent Decree and Prince George’s County may or may not head there
All MS4 General Permits are here https://mde.maryland.gov/programs/Water/StormwaterManagementProgram/Pages/storm_gen_permit.aspx

## Slide 25
Questions/Discussion