## Slide 1
Rich Batiuk
Associate Director for Science, Analysis and Implementation
U.S. EPA Chesapeake Bay Program Office
Chesapeake Bay Program Principals’ Staff Committee March 2, 2018
Adjustments to the Bay’s Assimilative Capacity & Determination of Additional Nitrogen and Phosphorus Loads
Notes: I would remove the Chesapeake Bay image altogether since you already a header image depicting the bay. I would move the logo to the left side of the text ”Chesapeake Bay Program Principals’ Staff Committee, December 19, 2017” since this is where our name is located. Also, widen the text box so that Decisions isn’t on a line by itself. This also gives a bit more breathing room between the title and the sub-text.

## Slide 2: Today’s Requested Policy Decisions
Approve West Virginia’s contingency language.
Approve West Virginia's request to reduce their Phase III WIP Planning Target from the PSC-approved 2 million pounds of nitrogen to 1.5 million.
Approve the approach to fully account for the additional pounds already provided to New York’s and West Virginia’s Phase III WIP Planning Targets.
Approve defining the Chesapeake Bay’s assimilative capacity as 196.5 million pounds of nitrogen and 13.75 million pounds of phosphorus.

## Slide 3: Updating Our Assessment of WV Loads
West Virginia received additional pounds under the Bay TMDL due to a lack of direct benefits from Bay water quality and principles of equity.
The 2 million pounds of nitrogen the PSC approved for West Virginia would have resulted in the state achieving its nitrogen goal in 2013.
West Virginia and the Chesapeake Bay Program Office worked together to determine whether the Phase 6 Model’s estimate of West Virginia’s delivered nutrient loads (according to the state’s Phase II WIP) would allow for a lower Phase III WIP planning target and reduce the burden on other jurisdictions.

## Slide 4: Updating Our Assessment of WV Loads
Results: West Virginia will agree to a 1.5 million pound increase in its nitrogen Phase III WIP Planning Target.
West Virginia asks the PSC to agree to the following contingency language:
  “In the event that circumstances occur that increases the loads resulting from West Virginia’s Phase II level of effort (ex. revised BMP efficiencies), or new directives are initiated to increase Partnership level of effort (ex. climate change, Conowingo), the Chesapeake Bay Program Partnership commits to West Virginia to provide the pounds of nitrogen necessary to remain at WV’s Phase II level of effort.”

## Slide 5: Confirming Additional Loads for New York
New York received additional pounds under the Bay TMDL due to a lack of growth and principles of equity.
Chesapeake Bay Program Office staff re-ran the PSC allocation methodology using a 1985 base year in place of the agreed-upon 2010 base year.
Results: Using the Phase 6 Model and up-to-date local data, the Chesapeake Bay Program Office confirmed New York was receiving the appropriate level of additional loads under the Bay TMDL—1 million pounds of nitrogen and 100,000 pounds of phosphorus.

## Slide 6: Sources of Additional Loads
The Bay’s assimilative capacity
  Are additional pounds of nitrogen and phosphorus available and still keep the 6% restoration variance in Maryland’s segment CB4?
Clean Air Act regulations
  Will regulations implemented between 2025 and 2030 reduce nitrogen deposition to tidal waters and the watershed?
  Can we account for these reductions beyond 2025?

## Slide 7: Reassessing the Bay’s Assimilative Capacity

## Slide 8: Location Matters
Susquehanna: 1 pound
Potomac: 1 ½ pounds
Rappahannock: 2 pounds
James: 7 pounds
Relative Effectiveness of Nitrogen Reductions

## Slide 9
Reassessing the Bay’s Assimilative Capacity
Where We Were at the December 19th-20th PSC Meeting:
195 TN, 13.7 TP

## Slide 10
Reassessing the Bay’s Assimilative Capacity
Where We are in Today’s PSC Meeting:
196.5 TN, 13.75 TP

## Slide 11: Sources of Additional Loads: The Bay’s Assimilative Capacity
Source of Additional Loads | New York | West Virginia | Reserve
Bay Assimilative Capacity Evaluation | 500,000 pounds N 50,000 pounds P | 1 million pounds N | 0

## Slide 12: Clean Air Act Regulations

## Slide 13: Accounting for the Deposition of Nitrogen to Tidal Waters Between 2025 and 2030
From 1985 through 2025, loads will fall from 21.5 to 15.6 million pounds.
By 2025, loads will be 100,000 pounds below the Bay TMDL allocation.
By 2030, loads will drop to 14.9 millions pounds: 800,000 pounds below the Bay TMDL allocation.

## Slide 14: Accounting for the Deposition of Nitrogen to Tidal Waters Between 2025 and 2030
These post-2025 estimates are based on existing regulations and programs in place by 2025 and fully account for growth in different sources of emissions over time (including agricultural animal production).

## Slide 15: Accounting for the Deposition of Nitrogen to Tidal Waters Between 2025 and 2030
Two exceptions must be noted in—but should not influence—our 2030 nitrogen reduction estimates.
  These estimates do include emission reductions that would have resulted from the Clean Power Rule.
  These estimates do not include emission reductions that will be necessary to meet the 2015 National Ambient Air Quality Standards (which will likely be higher than those that would have resulted from the Clean Power Rule).

## Slide 16: Sources of Additional Loads: Atmospheric Deposition to Tidal Waters
Source of Additional Loads | New York | West Virginia | Reserve
Bay Assimilative Capacity Evaluation | 500,000 pounds N 50,000 pounds P | 1 million pounds N | 0

## Slide 17: Sources of Additional Loads: Atmospheric Deposition to Tidal Waters
Source of Additional Loads | New York | West Virginia | Reserve
Bay Assimilative Capacity Evaluation | 500,000 pounds N 50,000 pounds P | 1 million pounds N | 0
Atmos. Dep. to Tidal Waters by 2030 | 500,000 pounds N 50,000 pounds P | 180,000 pounds N | 0

## Slide 18: Sources of Additional Loads: Atmospheric Deposition to Tidal Waters
Source of Additional Loads | New York | West Virginia | Reserve
Bay Assimilative Capacity Evaluation | 500,000 pounds N 50,000 pounds P | 1 million pounds N | 0
 | + | + | +
Atmos. Dep. to Tidal Waters by 2030 | 500,000 pounds N 50,000 pounds P | 180,000 pounds N | 0
Total | 1 million pounds N 100,000 pounds P | 1.18 million pounds N | 0

## Slide 19: Accounting for the Deposition of Nitrogen to the Watershed Between 2025 and 2030
From 1985 through 2025, 254 million fewer pounds of nitrogen will fall on the watershed.

## Slide 20: Accounting for the Deposition of Nitrogen to the Watershed Between 2025 and 2030
This table outlines the nitrogen load reductions that will take place in each jurisdiction’s portion of the watershed.
State | Pounds N
DC | 0
DE | 20,000
MD | 210,000
NY | 40,000
PA | 280,000
VA | 220,000
WV | 30,000
Total | 800,000

## Slide 21: Sources of Additional Loads: Atmospheric Deposition to Watershed
Source of Additional Loads | New York | West Virginia | Reserve
Bay Assimilative Capacity Evaluation and Atmos. Dep. to Tidal Waters by 2030 | 1 million pounds N 100,000 pounds P | 1.18 million pounds N | 0

## Slide 22: Sources of Additional Loads: Atmospheric Deposition to Watershed
Source of Additional Loads | New York | West Virginia | Reserve
Bay Assimilative Capacity Evaluation and Atmos. Dep. to Tidal Waters by 2030 | 1 million pounds N 100,000 pounds P | 1.18 million pounds N | 0
Atmos. Dep. to Watershed by 2030 | None | 320,000 pounds N | 390,000 pounds N

## Slide 23: Sources of Additional Loads: Atmospheric Deposition to Watershed
Source of Additional Loads | New York | West Virginia | Reserve
Bay Assimilative Capacity Evaluation and Atmos. Dep. to Tidal Waters by 2030 | 1 million pounds N 100,000 pounds P | 1.18 million pounds N | 0
 | + | + | +
Atmos. Dep. to Watershed by 2030 | None | 320,000 pounds N | 390,000 pounds N
Total | 1 million pounds N 100,000 pounds P | 1.5 million pounds N | 390,000 pounds N

## Slide 24
Questions?

## Slide 25: Today’s Requested Policy Decisions
First: We need to approve West Virginia’s contingency language.
  “In the event that circumstances occur that increases the loads resulting from West Virginia’s Phase II level of effort (ex. revised BMP efficiencies), or new directives are initiated to increase Partnership level of effort (ex. climate change, Conowingo), the Chesapeake Bay Program Partnership commits to West Virginia to provide the pounds of nitrogen necessary to remain at WV’s Phase II level of effort.”

## Slide 26: Today’s Requested Policy Decisions
Second: We need to approve West Virginia's request to reduce their Phase III WIP Planning Target from the PSC-approved 2 million pounds of nitrogen to 1.5 million.

## Slide 27: Today’s Requested Policy Decisions
Third: We need to approve our approach to fully account for the additional pounds already provided to New York and West Virginia’s Phase III WIP Planning Targets.
  Determine what to do with additional pounds.
    Keep as a reserve pending final decisions on the Phase III WIP Planning Targets at the May PSC meeting; or
    Return the remaining pounds to the jurisdictions for credit post-2025 for atmospheric deposition to watershed reductions.

## Slide 28: Today’s Requested Policy Decisions
Last: We need to approve defining the Chesapeake Bay’s assimilative capacity as 196.5 million pounds of nitrogen and 13.75 million pounds of phosphorus.
  These loadings will replace the 195 million pounds of nitrogen and the 13.7 million pounds of phosphorus agreed to at the December PSC meeting.

## Slide 29
Rich Batiuk
Associate Director for Science
U.S. EPA Chesapeake Bay Program Office
410-267-5731 (Work)
443-223-7823 (Mobile)
batiuk.richard@epa.gov
www.epa.gov/chesapeakebaytmdl
www.chesapeakebay.net