## Slide 1
TMDLs for PCBs
for the Delaware River Estuary
Thomas J. Fikslin, Ph.D., Manager
Modeling, Monitoring and Assessment Branch
Toxics Contaminant Workgroup Meeting
Chesapeake Bay Program
January 8, 2015
Notes: <number>

## Slide 2: Delaware Estuary
<number>
Notes: <number>

## Slide 3: Background
Delaware Estuary is 133 miles long and is bordered by DE, NJ and PA
1998 – All three states listed the Delaware Estuary as impaired requiring the development of TMDLs.
Spring 2000 – DRBC designated the lead agency to develop the TMDLs for PCBs by the court-ordered deadline of Dec. 15, 2003.
Major boundaries: Delaware River at Trenton, NJ; Schuylkill River; C&D Canal; and the Ocean.
Point sources: 94 industrial and municipal facilities, CSOs, and MS4s.
Tributaries: 22
Contaminated sites: ~ 50
Air flux and deposition.
<number>
Notes: <number>

## Slide 4
<number>

## Slide 5
<number>
Notes: <number>
Tetra – Hepta Homologs:
  82.4 – 92.7% of Total PCBs

## Slide 6
Median Ambient PCB Concentrations
Stage 1 - 2002 to 2003
Tetra through Hexa Homolog Distribution
0
200
400
600
800
1000
1200
1400
2
3
4
5
6
Estuary Zone
picograms per liter (pg/l)
Tetra
Penta
Hepta
Hexa
Water Quality
Criterion - 16 pg/L
<number>
Notes: <number>

## Slide 7: Percent Contribution of PCB and DxFs TEQs

## Slide 8: Themes
PCB TMDL Strategy
Importance of the Water Quality Target
Importance of Source Identification and Quantitation
Need for a Model
Importance of the Sediment Reservoir
Implementing Complex TMDLs for PCBs
<number>
Notes: <number>

## Slide 9: PCB Strategy Elements
  Determine the water quality targets for the TMDLs.
  Characterize PCB concentrations in the estuary ecosystem.
  Identify and quantify sources of PCBs to the Estuary.
  Determine the transport and fate of PCBs loads within the Estuary.
  Establish TMDLs and allocations for sources.
The strategy consists of nine elements:

## Slide 10: PCB Strategy Elements (cont.)
  Develop an implementation plan to reduce PCBs entering the Estuary.
  Increase environmental awareness of toxicity issues in the Estuary.
  Monitor long-term concentrations of PCBs in air, water and sediments of the Estuary.
  Monitor long-term concentrations and impacts to living resources of the Estuary.

## Slide 11: Importance of the TMDL Target
TMDLs must be based upon the most stringent water quality criteria applicable to the receiving water in order for the designated uses of the water body to be met.
In interstate waters like the Delaware Estuary, inconsistent uses and criteria complicate the identification of the most stringent criterion.
In the Delaware Estuary, criteria for the protection of human health and wildlife were potentially the most restrictive.
<number>
Notes: <number>

## Slide 12: Water Quality Criteria
 | Zones 2 & 3 | Zone 4 & Upper Zone 5 | Rest of Zone 5
Existing DRBC Criteria | 44.4 pg/l | 44.8 pg/l | 7.9 pg/l
Existing PCB criteria creates a critical point in Zone 5. This has significant effects on the available assimilative capacity (the TMDLs).
<number>
Notes: <number>

## Slide 13: Penta-PCB Water Column Concentrations at TMDL Loads, 100 year simulation
<number>
Notes: <number>

## Slide 14
44.4 pg/L
44.8 pg/L
7.9 pg/L
16 pg/L
Unused assimilative capacity
Fully utilize assimilative capacity
Notes: <number>

## Slide 15: Water Quality Criteria
DRBC staff has developed a revised water quality criterion of 16 pg/L that is applicable to all zones.
This criterion utilizes the 2000 U.S. EPA methodology for deriving human health criteria, and incorporates:
    the upper bound estimate of the cancer potency factor of 2.0 (mg/KG)/day,
    site-specific fish consumption rates, and
    a site-specific bioaccumulation factor.
<number>
Notes: <number>

## Slide 16: Why develop a Model?
  Gain understanding:
      Determine PCB load-response relationships.
      Determine principal controlling processes.
  Address management questions:
      Determine PCB TMDL for each zone.
      Allocate TMDLs among sources.
      Assess the impact of load reduction strategies.
<number>
Notes: <number>

## Slide 17: Principal Mass Loadings and Fluxes
<number>
Notes: <number>

## Slide 18: Delaware River PCB Model (DELPCB)
Modified version of DYNHYD5/TOXI5
EPA-supported and widely used for toxic chemical TMDLs and contaminated sediments.
Model formulations/code extensively tested and assessed with observations at numerous sites.
Recommend building upon modeling work already done on the Chesapeake Bay watershed (e.g., Potomac River)
<number>
Notes: <number>

## Slide 19: Delaware River PCB Model (DELPCB)
Represents water column and sediments
One-dimensional in longitude
  87 spatial segments
Time-variable
Hydrodynamics
  Tidal heights
  Chloride mass balance
Organic carbon sorbent dynamics
  Particulate carbon (biotic and detrital)
  Dissolved organic carbon
Penta, Tetra, Hexa and Hepta-PCB homologs
<number>
Notes: <number>

## Slide 20: Short-term Calibration for penta-CB
<number>
Notes: <number>

## Slide 21: Decadal Scale Calibration for penta-PCB
<number>
Notes: <number>

## Slide 22: Key Findings
The principal sources of PCB loadings are non-point source runoff, point sources and the mainstem Delaware River.
The flux of PCBs between the gas phase in the atmosphere and dissolved PCBs in the water is a significant process affecting the achievement of the TMDLs.
PCB loadings at head of tide (Trenton) have a significant influence in the tidal Delaware River.
Water column PCBs are strongly influenced by loadings and sediments.
<number>
Notes: <number>

## Slide 23: Summary points
Model for PCBs is developed and calibrated.
Model is scientifically credible.
Collaboration with Delaware Estuary TMDL Coalition
  Avoided adversarial process and a competing model
Model was used to develop Stage 1 PCB TMDL, but Stage 2 is necessary to address uncertainties.
Model can be extended to other contaminants and to other watersheds.
<number>
Notes: <number>
Other contaminants: Chlordane, dioxin, metals
Other watersheds outside of the Delaware Basin:
  Allegheny, Susquehanna, Monongahela, and
  Ohio Rivers

## Slide 24: Source Identification & Quantitation
Identifying and quantifying PCB sources using congener-specific analytical methods has several benefits:
  Allows prioritization of sources for load reductions.
  Identify unusual PCB congeners that may be of concern.
  Reduces the uncertainty in model inputs.
  Permits fingerprinting of sources.
  Allows permittees/site owners to track the effectiveness of pollutant minimization activities.
<number>
Notes: <number>

## Slide 25: Penta-PCB Load by Source Category Sept 2001 through March 2003
<number>
Notes: <number>

## Slide 26
N = 16
<number>
Notes: <number>

## Slide 27
N = 12
<number>

## Slide 28: Establishing TMDLs
TMDLs are estimates of the loadings of each of the PCB homologs that can enter the estuary and still meet the current water quality criteria. They are projected loadings from all sources based upon assumptions called design conditions.
Since current concentrations of PCB homologs are 500 times higher than the water quality criteria, the TMDLs and associated individual WLAs and LAs will be proportionately less.
<number>
Notes: <number>
TMDLs are, by nature, abstract. They do not reflect current loadings, but are the hypothetical loadings that should result in the achievement of water quality standards at all points in the estuary.
Other points:
In order to meet standards at all points in the estuary, some parts of the estuary will have to be less than the standard for that portion of the estuary.
Reducing loads from their current levels to their allocation under the TMDL is part of the implementation of the TMDL.

## Slide 29
Allocate 5% of each of the zone TMDLs to a margin of safety (MOS).
Allocate to the contaminated sites category.
Allocate the remainder of the zone TMDLs to a WLA portion and a LA portion based upon the current percentage contribution for each of the source categories to each zone during the period February 1, 2002 to January 31, 2003.
Summary of Approach
for Stage 1
<number>
Notes: <number>
Additional loading of PCBs to the estuary is dependent on:
  dilution by flows from other sources into the estuary, and
  loss of PCBs through fate processes occurring in the estuary.
Two of the source categories do not explicitly provide additional flows to the estuary and therefore do not provide assimilation capacity:
  atmospheric dry deposition and gas phase transfer of PCBs, and
  contaminated sites.
Ground and surface water flow from contaminated sites do occur, but these flows have not been adequately characterized and are not included in the current version of the penta-PCB model.
As a result, the assimilative capacity for these sources must be obtained from other source categories.

## Slide 30
Using the estuary-wide ratio of penta-PCBs to Total PCBs from ambient data collected in the Delaware Estuary, the zone-specific, penta-PCB TMDLs were scaled up using a fixed ratio of 1:4 to calculate the TMDL.
<number>
Summary of Approach
for Stage 1
Notes: <number>

## Slide 31: Ratio of Penta-PCBs to Total PCBs in Ambient Samples
<number>
Notes: <number>

## Slide 32: Allocation of the Assimilative Capacity at the Critical Location
Penta PCB Water Target
Assimilative Capacity by Sedimentation
0.500 pg/L
1.975 pg/L
Usable Assimilative Capacity
0.183 pg/L
2.292
pg/L
Trenton
Schuylkill
Zone 2
Zone 3
Zone 4
Zone 5
Contribution by the Mouth of the Bay and C&D Canal
MOS
C. Site
Open BC
<number>
Notes: <number>

## Slide 33: Stage 1 TMDLs for Total PCBs
Estuary Zone | TMDL | WLA | LA | MOS
 | mg/day | mg/day | mg/day | mg/day
Zone 2 | 257.4 | 5.0 | 239.5 | 12.9
Zone 3 | 17.8 | 4.9 | 12.0 | 0.9
Zone 4 | 56.7 | 5.2 | 48.7 | 2.8
Zone 5 | 48.1 | 13.3 | 32.4 | 2.4
Sum | 380.0 | 28.3 | 332.6 | 19.0
Notes: <number>
The larger TMDL in Zone 2 is due to the assimilation capacity provided by the Delaware River at Trenton.
Similarly, the larger LA in Zone 2 is due to the allocation to the Delaware River, while the larger Zone 4 allocation is due to allocation to the Schuylkill River.

## Slide 34: Approach for Establishing Stage 2 TMDLs
The approach for establishing Stage 2 TMDLs is different than that used in Stage 1.
Some of the reasons for this are:
  A revised human health criteria for total PCBs has been adopted that does not produce a sharp transition between zones.
  An alternative allocation procedure for both the aggregate WLAs and LAs, and the individual WLAs and LAs that is more equitable will be needed.
<number>
Notes: <number>

## Slide 35: Approach for Establishing Stage 2 TMDLs
  TMDLs for total PCBs for each zone will be the sum of the TMDLs for four homologs without extrapolation from Penta-PCBs.
  Additional source reduction strategies that result from either the PCB Minimization Plans required in Stage 1 or strategies developed by co-regulators (EPA Regions 2 and 3, states and DRBC) and stakeholders will be implemented. Focus is on point source permitting strategy.
<number>
Notes: <number>

## Slide 36: Progress to Date
DRBC implemented the Stage 1 TMDLs by requiring point sources to conduct additional monitoring using low level techniques (Method 1668A). The results of this monitoring have been submitted and assessed.
DRBC passed regulations in May 2005 requiring point source dischargers to submit and implement PMPs. 42 dischargers are initially required to submit the plans.
Regulations can be applied to any point and non-point source that the Commission determines has an “adverse impact” on the water resources of the Basin.
<number>
Notes: <number>

## Slide 37: Achieving Water Quality Criteria
Reductions in PCB loadings will not immediately result in lower ambient water concentrations or in reduced tissue levels of PCBs in resident fish species.
This is due to the continuing flux of PCBs from the sediments to the water column. As solids uncontaminated by PCBs settle to the bottom, this flux will ultimately reach equilibrium with the water column.
<number>
Notes: <number>
Maintenance dredging and dredging of hot spots could accelerate the process, and achieve the WQ criterion sooner.

## Slide 38
June 2021
June 2031
<number>
Notes: <number>

## Slide 39: Implementing the TMDLs
The nature of PCBs requires a long-term strategy for permitting point source discharges and addressing non-point sources.
Such a strategy is needed to gain acceptance by stakeholders and ensure continued progress in reducing PCBs.
In view of the uncertainty in data on PCB concentrations in point source discharges, need for additional PCB model refinements, and uncertainty in treatment technologies, adaptive implementation of the PCB TMDLs was proposed.
Notes: <number>
Hydrophobic - sorb to sediments
Persistence
Multiple point and non-point sources

## Slide 40: NPDES Dischargers included in PCB TMDLs
Total number of permittees = 102
Notes: NJ > half of all dischargers in part due to the number of small municipal treatment plants
However the DRBC retains oversight of the majority of dischargers.
DRBC is transitioning review of some of the smaller PMPs to the states when these requirements are placed into their NPDES permit
<number>

## Slide 41: Stage 1 Implementation Requirements
Required monitoring for 209 PCB congeners using Method 1668A.
  Developed specific data quality objectives: http://www.state.nj.us/drbc/quality/toxics/ pcbs/monitoring.html
Required development, approval and implementation of a Pollutant Minimization Plan for PCBs (PMPs).
http://www.state.nj.us/drbc/programs/ quality/pmp.html
Notes: In 2005, DRBC issued a monitoring request to 42 of the NPDES permittees and also passed regulations governing the applicability and specific requirements for PMPs.
<number>

## Slide 42: Stage 2 Implementation Requirements
Build upon the monitoring and PMP requirements of Stage 1 TMDLs.
Incorporate the concept of an Action Level.
  Purpose - to elicit a prompt response to elevated PCB concentrations above those achieved.
  Establish duration and magnitude of elevated concentrations.
  Document actions taken and return to PCB concentrations previously observed, or proposed actions to be included in a revised PMP.
Notes: <number>

## Slide 43: NPDES Permitting Strategy
Notes: <number>

## Slide 44: Other Proposed Elements of the Implementation Strategy
Non-Point Sources
  Strategies for addressing NPSs were included in the 2009 TMDL Implementation Plan publically noticed by DRBC.
  The strategies focus on identifying and prioritizing sources of PCBs in each non-point source category described in the plan.
  Existing authorities would be utilized to focus on water quality impacts and achieve the load allocations assigned to these sources.
Notes: Examples:
Lail Property
Scrap Metal Facility in Camden
<number>

## Slide 45: Incremental Progress
Reductions in Loadings from Non-Point Sources
  Removal of ~40,000 lbs. of PCBs from tidally-influenced wetland adjacent to tributary creek.
  Removal of ~8,000 lbs. from NPL industrial site.
  Inventory of Superfund sites - DelTriP http://www.state.nj.us/drbc/about/public/publications/ deltrip.html
In 2013, DE and NJ relaxed fish consumption advisories to 1 meal per year in Zone 5.
Ambient water concentrations did not change significantly as expected.
Notes: <number>

## Slide 46: 10 Dischargers Representing 90% of Point Source PCB Loadings in the Estuary
46 % reduction
46 % reduction
Notes: Facilities:
Valero Refining
PWD-NE
PWD-SW
PWD-SE
CCMUA
City of Wilmington
AMTRAK Race St./Penn Coach
U.S. Steel
Trenton
Dupont -Chambers Works
TMDL - 50 mg/day
<number>

## Slide 47: O&M Requirements
Why is O&M necessary?
  Prevention of backsliding i.e. increasing loading after an initial reduction
Example: US Pipe and Foundry
  Manufactured iron pipe from recycled and new material
  Stored scrap metal on-site
  Legacy site >100 years old
  DSN 004 - Storm water effluent contaminated with PCBs

## Slide 48: U.S. Pipe and Foundry
Year | PMP Initiatives | Analytical Results
2007 | Existing sedimentation basin no treatment | 118,923 pg/L
2008 | Sediment removed from basin and filtration system added | 847 pg/L
2009 | Filtration system failed and demolition of facility began | 47,651 pg/L
2010 | Demolition continues increasing sediment load | 94,821 pg/L
2011 | Demolition completed and rerouting of additional stormwater to sedimentation basin. Increased sediment trapping in stormwater drains | 35,086 pg/L
2012 | Filtration system under repair (during sample collection). Identification of remaining potential sources | 33,434 pg/L
2013 | Filtration system repairs completed. Continued system Maintence. Begin re-grading and seeding to reduce runoff | 1,519 pg/L

## Slide 49: Dischargers Approaching Individual WLAs
Degussa Corporation (NPDES #PA0051713)
  Manufactures inorganic industrial products
  Discharge is treated by Industrial Waste Water Treatment Plant
    Neutralized
    Solids removed
BP Paulsboro (NJPDES #NJ0005584)
  Former refinery, since demolished undergoing ground water remediation
  Discharge is treated by Groundwater Treatment Plant
    Air stripping
    Carbon filtration

## Slide 50: Atmospheric gas phase PCB concentrations
<number>

## Slide 51: Ambient Water Concentrations
Water Quality Criteria 16 pg/L
Notes: Due to the reservoir of PCBs in the sediment that continue to feed the water column, reductions in the water column are projected to take decades.
Note some improvement in lower Zone 2 and upper Zone 3.
Some improvement in Zone 6.
<number>

## Slide 52
<number>

## Slide 53: Summary and Conclusions
TMDLs for certain parameters (like PCBs) will require alternative approaches since they will require long-term strategies to achieve.
An adaptive management approach was developed for the PCB TMDLs for the Delaware River Estuary.
This approach has achieved a 46% reduction in loadings from NPDES sources, and significant loading reductions from non-point sources.
Development of an implementation strategy provides a degree of certainty for permittees.
Notes: <number>

## Slide 54
Contact Information:
thomas.fikslin@drbc.state.nj.us
(609) 883-9500, ext.253
Information on the TMDLs, model development, sampling and analytical information, and PMP requirements and resources are available on the DRBC website at:
www.drbc.net
<number>
Notes: <number>