## Slide 1
Methylmercury Production in Groundwater
Watershed Hg Research Program at SERC
Deposition
Transport
Watershed retention
Methylation
MDN site
MD00
Stream
Monitoring
Brandon Shores w/ FGD
Hg and MeHg
Flux from streams

## Slide 2: SERC SITE
We have continuously monitored Hg and MeHg fate and transport from the three first order Maryland coastal plain watersheds since 2007.
  We measure flow-weighted fluxes of total and MeHg, both in filterable and particulate phases, weekly, along with a suite of other parameters.
  The watersheds studied include three land-use types – forest, agriculture and mixed development.
Groundwater processes are studied using sets well transects in W110 and W109, and with periodic stream transects.
Wet deposition is measured locally at Mercury Deposition Network Site MD00.

## Slide 3: Goals
Assessment of watershed Hg and MeHg yields in the mid-Atlantic Coastal Plain
Assessment of MeHg production and its hydrologic and biogeochemical controls in shallow groundwater
Establishment of a baseline against which to assess any change in:
  Implementation of Hg emissions regulations in Maryland, the region, and the US
  Implementation of additional SOx/NOx/CO2 controls
  Land use
  Implementation of restorations/BMPs
  Changes in flow regime and temperature

## Slide 4: Acknowledgements
Maryland DNR PPRP 2007-2015
Construction award for Muddy Creek Regenerative Stormwater Conveyance 2014-2016
Smithsonian Estuarine Research Center 1971-2015
NSF ARRA Infrastructure award for SERC Ecosystems 2011-12
National Science Foundation grant DEB0351050 to AH and CG 2005-2007
CBT award for monitoring SERC RSC 2015-2018 to Jordan and Gilmour

## Slide 5
Example Date – Hg, MeHg, Stream flow
Weekly flow-weighted samples (refrigerated ISCOs)
Flow based on water depth in a v-notch weir (stilling well + rating curve)
Water depth triggers ISCO samples
Wide range of analytes including:
  Nutrients
  Anions (IC)
  base cations (ICP-OES)
  DOC and spectral parameters
  Particulate and filterable
  pH, alkalinity from grabs

## Slide 6
Weekly precipitation at SERC and area weighted water flux from watersheds

## Slide 7
Stream flow and yield

## Slide 8
Seasonality in MeHg production

## Slide 9
Filterable Hg and MeHg yields
MeHg and Hg yields are different among watersheds
But yields are not changing over time
Filterable (bioavailable) Hg and MeHg flux is highest from the forested catchment

## Slide 10
Differences in chemistry among watersheds

## Slide 11
Filterable Hg and MeHg flux normalized to flow

## Slide 12
Particulate Hg and MeHg yields
Yields are different among watersheds
Particulate yields are driven by flow
Highly erodible W109 has highest particle flux

## Slide 13
Hg and MeHg fluxes from coastal plain watersheds did not change appreciably over the study period, consistent with no change in Hg wet deposition
  The timing of any response in stream flux to changes in Hg deposition remains unknown
  Implementation of federal Hg and CO2 emissions standards may finally drive down Hg deposition in Maryland in the next decade
Land use and BMPs have strong effects on Hg and MeHg flux
  Forested watersheds transport more Hg and MeHg - perhaps due to higher dry deposition, perhaps due to DOC-enhanced transport
  Erodible landscapes transport much higher masses of both Hg and MeHg
  Wet bottom lands in the coastal plain can enhance MeHg production, and the amount is impacted by NO3:SO4 ratios, and seasonal rain patterns
Coastal plain bottom lands support MeHg production in shallow anaerobic ground waters, helped along by sulfate in soils
Conclusions

## Slide 14
Implications for Management
Erosion control practices should reduce Hg and MeHg fluxes to the Chesapeake and other receiving water bodies
Sulfate emissions controls should continue to reduce MeHg production in watersheds outside the coastal zone (where soils derived from marine sediments have naturally high SO4)
BMPs and restoration practices for NO3 removal should be examined and designed for minimal impact on MeHg production
Increasing rainfall intensity could exacerbate particulate Hg and MeHg fluxes

## Slide 15
Why continue?
The original goal of testing the impact of reduced emissions on Hg and MeHg in streams is still valid – and may be testable in the next several years as nationwide emissions drop.
Regenerative Storm Water Conveyance (RSC) installation in Muddy Creek (W101) in late 2015 will test how this restoration practice impacts MeHg production.
  Planned parallel testing in high impervious surfaces watersheds in the South River basin
Better evaluate the role of changing rainfall patterns, temperature and climate on Hg and MeHg in coastal plain watersheds.