## Slide 1
Thoughts on Mercury Monitoring Needs for the Chesapeake and its Watershed
Ongoing:
Hg in creel-sized fish in CB, impoundments and rivers
Human risk assessment and consumption advice
Based on fish size and species
Done in MD by MDE/DNR
Post raw data online/update data in EPA on-line fish tissue database?
Measurement of Hg in YOY fish
Earliest indicator of success/change in response to emissions controls, management practices, changing climate or whatever!
Done by MD by DNR/UMCBL
Post raw data online

## Slide 2
EPA National Listing of Fish Advisories
Fish Tissue Search
Sites with fish tissue Hg data
~500 records; 1991- 2001

## Slide 3
Mercury Monitoring Needs for the Chesapeake
Ongoing:
Hg wet deposition and air concentrations
Posted on MDN website/QA by NADP
Still missing a good indicator for “dry” deposition
Lack of sites in VA/DE
Rainfall, sulfate and nitrate deposition (NADP)
Seasonality of precipitation and deposition are changing
Posted on MDN website/QA by NADP
Coastal plain stream monitoring
@ SERC, weekly during flow
Provides response of stream Hg/MeHg flux to changing deposition, landuse, rainfall
Concurrent with other water quality monitoring
Post raw data online

## Slide 4
Mercury Monitoring Needs for the Chesapeake
Needed:
An ongoing measure program for riverine Hg and MeHg inputs to the Bay
Add toxics measurements to fall-line monitoring program?
Mercury emissions data from power plants made available on line, near-real time
Evaluation of non-power plant emissions sources in region
Sediment database for CB
Updated Hg and MeHg budgets for CB