## Slide 1: Application of Vertical Array Data for the 4D Interpolator
Rebecca Murphy
UMCES at CBP
rmurphy@chesapeakebay.net
Sustainable Fisheries Goal Implementation Team Meeting
Sept. 19, 2023

## Slide 2: 4-D interpolator development team
BORG = Bay Oxygen Research Group:
Leadership
  Peter Tango (USGS/CBP), Rebecca Murphy (UMCES/CBP), August Goldfischer (CRC/CBP)
Development to-date
  Elgin Perry (statistician); Jon Harcum and Erik Leppo (Tetra Tech); Angie Wei and Rebecca Murphy (UMCES/CBP)
Guidance, ideas, direction
  Gary Shenk and Breck Sullivan (USGS/CBP), Isabella Bertani and Richard Tian (UMCES/CBP), Kaylyn Gootman (EPA/CBP), Jim Hagy (EPA)

## Slide 3
From EPA 2003 Ambient Water Quality Criteria
Purpose: Build a tool for more complete criteria assessment
DO criteria that currently can be evaluated with existing approaches and data
*
*Note a 30-day mean 6 mg/L MSN value is evaluated for purpose of the WQ indicator.

## Slide 4
From EPA 2003 Ambient Water Quality Criteria
Purpose: Build a tool for more complete criteria assessment
With higher frequency interpolation tool and data
*

## Slide 5
Calendar Year | 2022 |  |  |  | 2023 |  |  |  | 2024 |  |  |  | 2025 |  |  |  | 2026 |  |  |  | 2027 |  |  | 
Calendar Quarter | Q1 Jan-Mar | Q2 Apr-Jun | Q3 Jul-Sep | Q4 Oct-Dec | Q1 Jan-Mar | Q2 Apr-Jun | Q3 Jul-Sep | Q4 Oct-Dec | Q1 Jan-Mar | Q2 Apr-Jun | Q3 Jul-Sep | Q4 Oct-Dec | Q1 Jan-Mar | Q2 Apr-Jun | Q3 Jul-Sep | Q4 Oct-Dec | Q1 Jan-Mar | Q2 Apr-Jun | Q3 Jul-Sep | Q4 Oct-Dec | Q1 Jan-Mar | Q2 Apr-Jun | Q3 Jul-Sep | Q4 Oct-Dec
Project Year | Year 1 |  |  |  | Year 2 |  |  |  | Year 3 |  |  |  | Year 4 |  |  |  | Year 5 |  |  |  | Year 6 |  |  | 
1. Development-daily estimates (Phase 1) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2. Develoment-hourly estimates (Phase 2) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3. Development - shallow water |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4. Development - GIS tasks |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5. Development -combined daily & hourly (Phase 3) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6. Development-criteria evaluation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7. Software |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8. Documenting |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
9. Training |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10. Year of Review |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
11. Operational |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4-D interpolator development timeline

## Slide 6: WQ Assessment with 4D interpolator
Observed data
GAMs
Mean daily prediction
Statistical simulation
Multiple feasible hourly realizations
WQ assessment
Attainment
tool
data
product
From Gary Shenk

## Slide 7: Uses of the Vertical Array data
Exploratory: Examine the DO cycles and patterns
Development of 4D hourly interpolation method, including both:
  Calibration
  Validation
Eventually:
  Criteria assessment in select segments, and
  Aid in estimation of high frequency variability in locations without monitoring

## Slide 8: Uses of the Vertical Array data
Exploratory: Examine the DO cycles and patterns
Development of 4D hourly interpolation method, including both:
  Calibration
  Validation
Eventually:
  Criteria assessment in select segments, and
  Aid in estimation of high frequency variability in locations without monitoring

## Slide 9: Exploratory work
As array data becomes available, we are using it to examine short-term variability, and its impact on:
The statistical techniques we use to build the interpolator
Pycnocline computation (determining designated use)
Spatial co-variability of high frequency dynamics
What we can learn about implementing short-term criteria evaluation
9
9
OW
DW
DC
OW
DW
Note: on 8/9/22 the array data had an 8-hour gap
Example: East Goose Vertical Array Data (grey lines) at dates with fixed station sampling (black line) in 2022

## Slide 10: Exploratory work
As array data becomes available, we are using it to examine short-term variability, and its impact on:
The statistical techniques we use to build the interpolator
Pycnocline computation (determining designated use)
Spatial co-variability of high frequency dynamics
What we can learn about implementing short-term criteria evaluation
10
10
10
10
10
Example: Cumulative Frequency of DO levels in each Designated Use from East Goose Profiler DO in 2022

## Slide 11: Uses of the Vertical Array data
Exploratory: Examine the DO cycles and patterns
Development of 4D hourly interpolation method, including both:
  Calibration
  Validation
Eventually:
  Criteria assessment in select segments, and
  Aid in estimation of high frequency variability in locations without monitoring

## Slide 12: Method development with high frequency data
Example: Current processing technique from Tetra Tech team using East Goose’s array in 2022 at 9m
From Jon Harcum (Tetra Tech)
Download, read codes, plot
Interpolate short gaps and delimit blocks by longer gaps

## Slide 13: Method development with high frequency data
Example: Wavelet analysis of gap-filled data to identify cycles
From Elgin Perry
Download, read codes, plot
Interpolate short gaps and delimit blocks by longer gaps
Do a wavelet analysis for each depth and block
Identify common cycles at each depth (tidal, daily, etc)

## Slide 14: Method development with high frequency data
Example: Fourier analysis with just daily cycle to fit hourly DO (DOh)
From Elgin Perry
h = hour 1:24
coefficients
Download, read codes, plot
Interpolate short gaps and delimit blocks by longer gaps
Do a wavelet analysis for each depth and block
Identify common cycles at each depth (tidal, daily, etc)
Fit coefficients of Fourier analysis for each observed cycle
Explore for relationships to other features (depth, month, DO, flow)

## Slide 15: Method development with high frequency data
d1, t1
d2, t1
d3, t1
d1, t2
d2, t2
d3, t2
…
…
“4d” Spatial & temporal estimates of DO
Download, read codes, plot
Interpolate short gaps and delimit blocks by longer gaps
Do a wavelet analysis for each depth and block
Identify common cycles at each depth (tidal, daily, etc)
Fit coefficients of Fourier analysis for each observed cycle
Explore for relationships to other features (depth, month, DO, flow)
Ultimately: generate hourly DO estimate bay-wide that are calibrated and validated with observed data

## Slide 16: Locations?
Discussion is ongoing for location of future arrays with the Hypoxia Collaborative Team.
4-D team thoughts (input here from Peter Tango):
Pairing stations within a region may be useful, including:
  Spanning the boundaries of hypoxic zone
  Pairing stations laterally in a wide segment
  Making shallow-to-deep station matches
Duration considerations:
  Year-round is ideal b/c there are 12-month criteria
  3-year periods important for assessment
  Long-term deployments will be useful for dynamic modeling needs and tracking trends related to climate change
But almost any location will be helpful for our 4D method development because we have many gaps in high frequency DO knowledge. Collaborating with fisheries needs makes a lot of sense.
 These and more diverse needs may lead to hybrid approach of some long-term stations and some 3-year rotating stations.