## Slide 1
Rising Watershed and Chesapeake Bay Water Temperatures—Ecological Implications and Management Responses
STAC Workshop Draft Findings
Habitat GIT
May 5, 2022
Presented by Katie Brownson, USFS

## Slide 2
Chesapeake Bay tidal and non-tidal water temperatures have been increasing.
Rice and Jastram, 2015)

## Slide 3
Air temperatures
Ocean temperatures
Sea level rise
River temperatures
Source: Hinson at el. 2021
Increasing tidal water temperatures have been driven largely by atmospheric forcings
and the warming ocean boundary

## Slide 4
Non-tidal water temperature
Streamflow
  Baseflow
  Withdrawals (from surface or groundwater)
  Local hydrology (presence of dams, floodplain connectivity, etc.)
  Hydraulic resistance
  Upstream and riparian land use
  Groundwater inputs
  Degree of infiltration
  Rainfall
Runoff temperature
  Sources of water (farm ponds, municipal, mining and industrial discharge, snowmelt, etc.)
  Upstream and riparian land use
  Degree of infiltration
Heat transfer from channel substrate
  Substrate composition (bedrock vs. gravel)
  Hyporheic exchange
  Residence time in hyporheic zone
Groundwater inputs
  Hyporheic exchange
  Groundwater temperature
  Degree of infiltration
  Groundwater residence time
  Legacy sediment
  Underlying geology
Channel temperature buffering capacity
  Surface area: volume ratio
  Channel form
  Large woody debris
  Instream vegetation
  Water clarity
  Stream size
Air temperature
  Direct solar radiation
  Canopy cover
  Ambient air temperature
Increasing stream and river temperatures have been driven by rising air temperatures, but other drivers have a strong influence

## Slide 5
Watershed
Tidal & Watershed
Mitigation
Lowering of Water Temps
Adaptation
Minimize Impacts & Adjust
Submerged Aquatic Vegetation (SAV)
Oysters
Blue Crabs
Forage
(Menhaden, Bay anchovy, benthic invertebrates)
Striped Bass
BMPs
Brook Trout
Conservation
Land use practices

## Slide 6: Watershed
Trends, Drivers, Ecological Impacts, Management Implications &
Draft Recommendations
Leads: Katie Brownson, U.S. Forest Service & Rebecca Hanmer, Forestry Workgroup Chair

## Slide 7: Ecological Impacts - Species
Strongest negative impacts on coldwater species (e.g., trout, sculpin) and their habitats (esp. where streams aren’t driven by groundwater )
Watershed-wide, warmwater aquatic species are most common. Although more tolerant to temperature increases, they are sensitive to extreme temperatures including rapid changes and to indirect effects (e.g., invasives, pathogens) from higher temps.
More study needed of temperature effects on lower foodweb
    Algae, biofilms, zooplankton
    Macroinvertebrates
    Freshwater mussels & host species

## Slide 8: Ecological Impacts - Other Stressors
Co-occurring Stressors
  Low dissolved oxygen
  Invasive species
  Algal blooms
  Bacterial/viral outbreaks
  Distribution & toxicity of other
pollutants (e.g., heavy metals,
pesticides, ammonia, etc.)
  Expansion of invasives
Photo credit: Driscol Drones

## Slide 9: Day 2 Themes for Discussion
Coldwater fisheries and habitats
Rural waters and habitats
Urban waters and habitats
Cross-watershed topics
  State temperature water quality standards (WQS), monitoring and implementation
  Monitoring and modeling
Photo credit: Joel Prince, NASF

## Slide 13: State Temperature Water Quality Standards (WQS)
Modernize WQS to make them more effective to combat rising water temperatures
Strengthen anti-degradation measures
Improve criteria to reflect a better understanding of thermal tolerances and ecology for a broader suite of species
Improve interstate cooperation through information-sharing, problem solving and monitoring-modeling support

## Slide 14: Monitoring, Modeling and Science Needs
Better use existing monitoring data and mapping tools
Improve monitoring networks to better include small streams and incorporate more continuous data collection
Evaluate the relative influence of BMPs and habitat restoration on water temperature, including cost-effectiveness
Develop models that better simulate land use and groundwater effects on local steam temperatures to better understand how stream temperature and living resources will respond to management
Establish multi-species prioritization tools and science-based targets for restoration and conservation to mitigate rising water temperatures

## Slide 15: TIDAL
Trends, Drivers, Ecological Impacts, Management Implications &
Draft Recommendations
Leads: Julie Reichert-Nguyen & Bruce Vogt, NOAA and Rich Batiuk, CoastWise Partners

## Slide 16
Varying Effects and Sensitivities to Rising Water Temps for Tidal Species
- biological / - ecosystem
+ biological / - ecosystem
+ biological / + ecosystem
- biological / + ecosystem
-
+
+
-
Biological
Ecosystem

## Slide 17
Science Needs – Better Understanding of Ecosystem-Level Effects, Multiple Stressors & Extreme Events on Survival & Habitat
Lower oxygen solubility in water
Higher water temperature
Higher remineralization rate = more nutrients for algae growth
More stratified water column
All combined = even lower dissolved oxygen
Source: Mazzini and Pianca 2022
Effects of reduced water clarity & salinity from increased precipitation and habitat loss/change on SAV & oysters
Effects of SAV community changes on habitat-use by fish and crabs
Changes in the intensity, duration, & frequency of marine heat wave events & effects on survival

## Slide 18: Day 2 Themes for Discussion
Ecosystem-based management
Multiple stressors
Nearshore habitats
New temperature regime

## Slide 19: Management Recommendations (DRAFT)
Ecosystem-Based Management
(3) Continue water quality improvement to support SAV essential fish habitat
(1) Adjust within same season fisheries catch limits using two prong approach:
  1) develop management triggers based on temperature thresholds for determining seasonal closures and
  2) Incorporate an educational/human behavioral warming tool to communicate when fish are most stressed/vulnerable & how to modify fishing behavior outside of closures

## Slide 20: Management Recommendations (DRAFT)
Nearshore Habitats
(3) Target use of natural/green infrastructure where ecological & climate resilience benefits are highest
(2) Amplify the urgency to manage shoreline development & condition based on ecological thresholds already established for SAV, blue crab and fish

## Slide 21: Management Recommendations (DRAFT)
Multiple Stressors
(3) Implement TMDL to its fullest potential & better connect to living resource outcomes
(2) Develop a public facing heat wave warning system that incorporates dissolved oxygen and is linked to habitat preferences of key species such as striped bass, blue crabs, oyster, and SAV

## Slide 22: Management Recommendations (DRAFT)
New Temperature Regime
(1) Improve long-term monitoring networks to better connect to managing living resources
(6) Explore ways to support fisheries in the development of more strategic, long-term climate predictions for management

## Slide 23: Next Steps
Steering Committee will review & synthesize information, including management recommendations and associated science needs, from synthesis papers and both workshop days and draft final report
Participant review of draft report (~May-June 2022 timeframe)
Release final report (~summer 2022 timeframe)
Conduct outreach with Bay Program and partners to discuss strategies to implement the report’s recommendations

## Slide 24: Watershed Acknowledgements
Synthesis Element #1 Paper (Water Temperature Effects on Fisheries and Stream Health in Nontidal Waters): Stephen Faulkner, Kevin Krause, Rosemary Fanelli, Matthew Cashman, Than Hitt and Benjamin Letcher, USGS; Frank Borsuk and Greg Pond, EPA
Synthesis Element #1 Addendum (Temperature Criteria in CBP Jurisdictions' Water Quality Standards and Information on Warmwater Species): Rebecca Hanmer, EPA-retired; Jonathan Leiman, Maryland Department of the Environment; Daniel Goetz, Maryland Department of Natural Resources; Robert Breeding, Virginia Department of Environmental Quality; and Matthew Robinson, DC Department of Energy and Environment
Synthesis Element #4 Paper (Watershed Characteristics and Landscape Factors Influencing Vulnerability and Resilience to Rising Stream
Temperatures): Renee Thompson, USGS; Nora Jackson, CRC/CBP; Judy Okay, J&J Consulting; Nancy Roth, Tetra Tech; Sally Claggett, USFS
Synthesis Element #5 Paper (Trends): Rich Batiuk, CoastWise Partners; Nora Jackson, CRC/CBP; John Clune, USGS; Kyle Hinson, VIMS; Renee Karrh, Maryland Department of Natural Resources; Mike Lane, Old Dominion University; Rebecca Murphy, University of Maryland Center for Environmental Science/CBP; and Roger Stewart, Virginia Department of Environmental Quality
Synthesis Element #6 Paper (Model Projections): Rich Batiuk, CoastWise Partners; Gopal Bhatt, Pennsylvania State University/CBP; Lewis
Linker, U.S. EPA CBP; Gary Shenk, USGS/CBP; Richard Tian, University of Maryland Center for Environmental Sciences/CBP; and Guido Yactayo, Maryland Department of the Environment
Synthesis Element #7/8 Paper (Impacts of BMPs and Habitat Restoration on Water Temperatures): Katie Brownson and Sally Claggett, USFS; Tom Schueler, CSN; Anne Hairston-Strang and Iris Allen, Maryland Department of Natural Resources-Forestry; Frank Borsuk and Lucinda Power, EPA; Mark Dubin, UMD; Matt Ehrhart, Stroud; Stephen Faulkner, USGS; Jeremy Hanson, VT; Katie Ombalski, Woods & Waters
Consulting
Synthesis Element #10 Paper (Monitoring): Peter Tango, Breck Sullivan, John Clune, and Scott Phillips, USGS

## Slide 25: Tidal Acknowledgements
Synthesis Element #2 Paper (Tidal Fisheries and Habitat Impacts): Bruce Vogt, Jay Lazar, and Emily Farr, NOAA; Mandy Bromilow, NOAA Affiliate; Justin Shapiro, CRC
Synthesis Element #3 Paper (SAV Impacts): Brooke Landry and Becky Golden, Maryland DNR; Marc Hensel and Chris Patrick, VIMS; Dick Zimmerman and Rhianne Cofer, Old Dominion University; Bob Murphy, TetraTech
Synthesis Element #5 Paper (Trends): Rich Batiuk, CoastWise Partners; Nora Jackson, CRC/CBP; John Clune, USGS; Kyle Hinson, VIMS; Renee Karrh, Maryland Department of Natural Resources; Mike Lane, Old Dominion University; Rebecca Murphy, University of Maryland Center for Environmental Science/CBP; and Roger Stewart, Virginia Department of Environmental Quality
Synthesis Element #6 Paper (Model Projections): Rich Batiuk, CoastWise Partners; Gopal Bhatt, Pennsylvania State University/CBP; Lewis Linker, U.S. EPA CBP; Gary Shenk, USGS/CBP; Richard Tian, University of Maryland Center for Environmental Sciences/CBP; and Guido Yactayo, Maryland Department of the Environment
Synthesis Element #9 Paper (Indicators): Julie Reichert-Nguyen and Bruce Vogt, NOAA; Mandy Bromilow, NOAA Affiliate; Ron Vogel, UMD for NOAA Satellite Service; Breck Sullivan, USGS; Anissa Foster, NOAA-CRC Internship Program
Synthesis Element #10 Paper (Monitoring): Peter Tango, Breck Sullivan, John Clune, and Scott Phillips, USGS

## Slide 26: Thank you! Questions?