## Slide 1
Denice Wardrop (CRC) and Kurt Stephenson (VT)
August 24, 2023
Presentation to STAR
Refresher Reel: Achieving Water Quality Goals in the Chesapeake Bay: Comprehensive Evaluation of System Response (CESR):

## Slide 2
CESR Report
Self-initiated
Inclusive of STAC Membership
  Multiple levels of internal and agency review
  Over 50 contributors with unanimous STAC inclusion
  Main report (Co-editors and Steering Committee) plus 3 “Resource Documents”

## Slide 3
Chesapeake Bay Agreement: Restoration Goals
Sustainable Fisheries
Vital Habitat
Water Quality
Toxic Contaminants
Heathy Watershed
Climate Resiliency
Land Conservation
Stewardship
Public Access
Environmental Literacy
Water Quality Standards
Designated Uses
Water Quality Criteria
Dissolved Oxygen, Water clarity/SAV,
& Chl-a
across 5 habitats
TMDL: Stressor Reduction Goals
Targets: Nitrogen, phosphorus, sediment
TN: 214.6 m/lbs/yr TP: 13.4m lb/yr TSS: 18,587m lb/yr
Public Policy
Biological, Physical, and Social System Response
Achieving TMDL:
Are implementation policies and management actions sufficient to achieve nitrogen, phosphorus and sediment goals in the TMDL?
Implementation Policies
Federal permitting
Fed/State nonpoint programs
Funding
TMDL accounting & accountability
Achieving Water Quality Standards
Are nutrient & sediment reductions producing expected water quality response?
Living Resource Response
How are living resources responding to changing water quality conditions?

## Slide 4
System Response to Meeting Bay Water Quality Standards
SAV wetlands, shorelines
Access to habitat (fish passage) Bottom conditions
WQ Criteria & Assessment
External Factors
TMDL
Designated Use

## Slide 5
Summary of CESR Findings and Implications
Achieving TMDL
Achieving Water Quality Standards
Living Resource Response
Findings: Nonpoint source programs are not generating the scale of reductions needed to achieve TMDL
Implications: To substantially improve nonpoint source outcomes will require new programs and approaches
Findings: Bay water quality is improving, but the magnitude of the improvement appears to be lagging behind expectations
Implications: Full (100%) achievement of Bay water quality standards is a distant and doubtful.
Findings: The impact of WQ improvements on living resources depends on where WQ improvements occurs, antecedent conditions, & impact varies across species.
Implications: Potential to increase the impact on living resources from our WQ and restoration investments.
Overarching Finding: Complex problem with tradeoffs, uncertain outcomes, and no single “silver bullet” answer
Overarching Implication: Experiment, learn, and adapt

## Slide 6: Implications
Full attainment may not be necessary to improve and support living resources goals
Notes: Gaps are shifting the cost of attainment curve
Costs expected to increase rapidly
May never intersect full attainment.

## Slide 7
CAST
CAST
Flow normalized Load
Flow normalized Load
Difference between expected and observed outcomes
Response gap
Notes: There is a disconnect….
Many in the CBP believe that CAST under credits BMPs. Adding more BMPs to CAST will only make the response gap larger… Adding more BMPs to CAST will make it easier on paper to meet TMDL and further from achieving outcomes in the real world.

## Slide 8
Nutrient Mass Balance
Source: USGS Sparrow Model Output
Moyer et al. 2107, Webber, 2017

## Slide 9
Basin
9,000 acre sub-watershed
Improve tools and incentives for targeting
Nutrient loads are highly variable across the landscape across multiple scales (including across land managers).
25 acre parcel
Quartile | Total P balance (kg/ha)
Minimum | -30.9
1st Quartile | 1.5
Median | 12.4
3rd Quartile | 18.7
Maximum | 97.6
Total phosphorus balance across 58 dairy farms in Shenandoah Valley Virginia, 2018
(Source: Pearce & Maguire 2020)
Notes: Studies suggest 5-20% of the land area generates 50-90% or more of runoff and nonpoint source loads
Within fields, nutrient losses may be confined to relatively small areas that with the correct targeting and incentives may be easily treated.
Others have found that targeting BMPs to sites with higher pollution potential can improve cost effectiveness of pollution reduction efforts

## Slide 10
Incentivize Outcomes
Cover crops
Livestock Exclusion Fencing
Denitrifying Bioreactor
Low upfront installation costs Private benefits
High up front installation costs
No private benefits

## Slide 11
Finding: DO Response across Habitats
Expected and realized relationships between TN loads and DO criteria attainment for open water, deep water, and deep channel habitat, calculated as 3-year running mean observed values (blue diamonds) and expected responses from estuary model (orange dots) for the same time periods. Yellow squares are 10-year means of the observed data.
Response gap
Response gap

## Slide 12: Trajectories of Response
Increasing Nutrient Loads
Hypoxia Intensity
Degradation
Possible Recovery Trajectories
Nutrient loading at which system fell short of attainment
Nutrient loading at which system will reach attainment
Attainment of WQS
Trajectory unable to return to initial state
Climate change
Tipping points
Biotic communities
Land use/land cover
Notes: Here is my thinking on a variant of your graphic… including a return to neverland idea.

## Slide 13
Land Manager
Offer $ based on portion of installation cost of a practice
$
Cost
BMP
Voluntary Financial Assistance: Cost-Share
Nonpoint Source Implementation Policy

## Slide 14: Achieving TMDL: Finding: Nonpoint source programs are not generating the scale of reductions needed to achieve TMDL
Two Challenges
1) Nonpoint source programs not generating sufficient levels of adoption/behavior change
2) The actions/practices being implemented may not be as effective as expected in producing pollutant reductions

## Slide 15
Nonpoint source programs are not generating enough adoption/change (“implementation gap”)
Chart: 
| Nonpoint | Wastewater | Atmospheric | Septic
 | 157.3277 | 29.9693 | 17.0725 | 7.8454
Controllable N Loads to the Chesapeake Bay, 2021 (estimated by CAST Model)
Ag
Urban
Millions of lbs/yr
+50 million lb/yr N reduction needed
Total nonpoint source reduction achieved from 2009-2021

## Slide 16
Nonpoint source programs may not be as effective as expected
Estimated flow-normalized total and source sector TN and TP fluxes to the Chesapeake Bay for the CAST and SPARROW models
Ator et al. 2020
Nitrogen
Phosphorus
Notes: The nonpoint source challenge NPS control efforts (BMPs) are effective, but response has not (yet) been detected i) Legacy Nutrients and Lag Times Mask BMP effectiveness ii) NPS BMPs and NPS policies are not as effective as predicted a) BMP Performance Effectiveness Estimates b) Spatial distribution of BMPs with respect to pollutant sources c) Uncertainty both in behavioral response to nonpoint source control measures and in BMP effectiveness

## Slide 17
Source: Mason and Soroka, 2022
Total Phosphorus Yields at the RIM sites
Black Line is flow Normalized Yield, 1985-2021
Notes: Progress? Maybe in the light of climate change, population growth, agricultural intensification, etc

## Slide 18: Achieving TMDL: Implication: To substantially improve nonpoint source outcomes will require new programs and approaches
Ideas to improve nonpoint source program effectiveness

## Slide 19
Incentive Programs
Land Manager
Offer $ based on portion of installation cost of a practice
$
Cost
BMP
Voluntary Financial Assistance: Cost-Share
Land Manager
Offer $ based on producing an outcome
Revenue $
Cost
Behavior change
Payment for outcomes/success
Outcome

## Slide 20
Encourage Institutional/policy Innovation
The Sandboxing Process (Figure adapted from Higgins and Male, 2019)
Sandboxing
Ideas for what to “Sandbox”
TMDL accounting & accountability (alternative to CAST)
Types of outcome-based incentive programs
Alternative regulatory programs

## Slide 21: Achieving Water Quality Standards:
Findings: Bay water quality is improving, but the magnitude of the improvement appears to be lagging behind expectations

## Slide 22: Achieving Water Quality Standards:
Implications: Full (100%) achievement of Bay water quality standards is a distant and doubtful.
Implementation Cost (expectations)
Costs to meet WQS ($)
% Achievement of Water Quality Standard
20% 40% 60% 80% 100%
Full Attainment
Costs of Achieving TMDL and Water Quality Criteria
Implementation Cost (w response gaps)

## Slide 23: Living Resource Response

## Slide 24: Living Resource Response
Indicator of living resource abundance
% Attainment of WQS
Full attainment
Living resource response to attainment of water quality standards
20% 40% 60% 80% 100%
Findings: The impact of WQ improvements on living resources depends on where WQ improvements occurs, antecedent conditions, & impact varies across species.

## Slide 25: Boosting Living Resource Response

## Slide 26: Living Resource Response
Implications: Potential to increase the impact on living resources from our WQ and restoration investments

## Slide 27: Implications
Full attainment may not be necessary to improve and support living resources goals
Notes: Gaps are shifting the cost of attainment curve
Costs expected to increase rapidly
May never intersect full attainment.