## Slide 1: Local Planning Process…
Citizen Advisory Committee
May 23, 2018

## Slide 2
What and Why
  Planning Targets, Local Goals
  Progress
  Why is this Important?
Where – By County
Who (This Means Us) and When
  Action items, Measurable outputs and outcomes, timelines
  Milestones, Progress Reporting, Indicators
  Other
How
  Local Planning Goal Workgroup Toolbox
  Watershed Agreement Outcomes and Indicators
  Bay Program and SRBC Resources and Modeling Tools
Objectives – The Phase 3 WIP Story

## Slide 3: How do we determine “local”?
Step 1: Convert any Chesapeake Bay “diet” into a local PA stream diet.
  CBP Model has estimates of nutrient and sediment delivery from the field to local streams through large rivers and to the Bay.
  Pounds of pollutant delivered to the Bay can be expressed as pounds delivered to local streams using these factors.
  If 73.18 M lbs of Nitrogen delivered to the Bay is PA’s Chesapeake Bay “diet”, that number is equivalent to 108.06 M lbs of Nitrogen delivered to local streams.
73.18 M Lbs
(Bay)
111.06 M Lbs
(Local Streams)
Source:
Matt Johnston, University of Maryland

## Slide 4
Chart: 
Source:
Matt Johnston, University of Maryland
Rivers - 122
Counties - 42
Sub-Basins - 6
Land-River Segments (LRSEG) - 505
Step 2: Choose a geography to split up the diet.
    Small watershed – Swatara Creek (122)
    County – Berks (43)
    Sub-basin – Lower Susquehanna River (6)
    River basin – Susquehanna River (3)

## Slide 5: Where Should Efforts be Targeted?
Tier 1 - First 25% of Reductions
Tier 2 - Second 25% of Reductions
Tier 3 - Third 25% of Reductions
Tier 4 - Last 25% of Reductions
Source:
Matt Johnston, University of Maryland

## Slide 6
Chart: Estimated Reductions in Lbs of Nitrogen Delivered to PA Streams as of 2016, and Additional Reductions Needed by 2025 (Numbers Draft)
| Lancaster | York | Franklin | Lebanon | Cumberland | Dauphin | Centre | Bedford | Adams | Northumberland | Perry | Huntingdon | Columbia | Snyder | Mifflin | Lycoming | Schuylkill | Juniata | Union | Bradford | Chester | Clinton | Tioga | Susquehanna | Berks | Clearfield | Fulton | Blair | Lackawanna | Cambria | Montour | Luzerne | Sullivan | Potter | Wyoming | Somerset | Indiana | Elk | Cameron | Wayne | Mckean | Jefferson | Carbon
Background Load (E3) | 9724962.4 | 5440687.2 | 3277852.3 | 2099289.6 | 2842603 | 2883204.9 | 3362221.5 | 2432988.7 | 2385532.7 | 2455599.9 | 2037866.6 | 2321086.2 | 2024947.3 | 1512235.7 | 1433619.7 | 3360782.7 | 1769474.7 | 1409620.3 | 1223186.5 | 3009030.3 | 729139.1 | 2178542.2 | 2042948.5 | 1961079.9 | 640146.8 | 2570092.2 | 1014065.1 | 2064988.8 | 1444447.2 | 932298.5 | 672514.9 | 2882604 | 854246.2 | 1201174.6 | 970202.5 | 339546 | 173988.9 | 551911.6 | 719145.9 | 128457.2 | 42601.3 | 4946.9 | 9514.6
Possible Reductions not Required | 5841793.2369 | 2607356.9716 | 1563486.2972 | 1067168.2931 | 1252507.7609 | 1331286.0572 | 819771.0839 | 672275.4766 | 876421.1741 | 1050930.816 | 632784.5453 | 644123.4058 | 677678.3026 | 573491.7778 | 513956.7941 | 791773.8747 | 570943.6814 | 487729.3564 | 464112.7442 | 864261.2503 | 328634.0128 | 380830.9361 | 396853.9604 | 341883.6723 | 242181.1442 | 385385.4108 | 251300.1481 | 1124633.1239 | 665652.3702 | 204482.875 | 251221.3506 | 1293772.1481 | 110159.5691 | 117084.7685 | 336499.2206 | 58534.7422 | 37578.302 | 38505.2369 | 40242.3485 | 16823.4552 | 1576.569 | 969.1267 | 5058.3748
Reductions Still Needed | 11498939.3631 | 4301996.0284 | 3292585.3028 | 2350370.6069 | 2270866.3391 | 1913181.7428 | 1834508.0161 | 1614758.2234 | 1585323.2258 | 1578992.684 | 1523169.8547 | 1445422.0942 | 1443648.8975 | 1431776.9222 | 1224937.9059 | 1160496.1253 | 1123412.0186 | 1059762.7436 | 985662.6558 | 950185.0497 | 922496.0872 | 884603.5639 | 883241.6396 | 826435.8277 | 672460.0558 | 658970.6892 | 648590.5519 | 562056.2761 | 523900.1298 | 505023.025 | 492924.9494 | 477392.8519 | 325740.8309 | 270915.3315 | 178549.8794 | 156119.7578 | 99446.298 | 97417.5631 | 86057.0515 | 41258.2448 | 4003.031 | 2665.3733 | 0
Reductions as of 2016 Progress V9 | 7235595.7 | 4059755 | 1721489.6 | 1072020.6 | 1745905.5 | 2356230.8 | 794484.4 | 541218.2 | 1225345.1 | 1791325.2 | 506159.8 | 620271.1 | 729654.3 | 407401.8 | 423313.1 | 1378709.7 | 707595 | 504377.3 | 502739.3 | 1821486.6 | 131427.8 | 336715 | 389462.5 | 269979.5 | 104210.9 | 576954 | 157324.9 | 3044623.7 | 1610836.1 | 150750.2 | 312737.8 | 3671713.2 | 27539.1 | 104573.6 | 900597.6 | 31600.2 | 21066.7 | 26068.1 | 42999.5 | 12694.3 | 1053 | 442.6 | 17630.2
Loads Already Reduced as of 2016.
Reduction Needed from 2016.
Controllable Load that does NOT Need to be Reduced.
Loads that are Uncontrollable
Purpose of the Phase III WIP is to describe programs and policies that will eliminate the green bar in each county (or geography of choice).
Tier 1 (First 25% of Reductions)
Tier 2 (Second 25% of Reductions)
Tier 3 (Third 25% of Reductions)
Tier 4 (Final 25% of Reductions)
Source:
Matt Johnston, University of Maryland

## Slide 7
Chart: Estimated Reductions in Lbs of Nitrogen Delivered to PA Streams as of 2016, and Additional Reductions Needed by 2025
| Lancaster | York | Franklin | Lebanon | Cumberland | Dauphin | Centre
Loads that are Uncontrollable | 9724963 | 5440687 | 3277852.25 | 2099289.5 | 2842603 | 2883205.25 | 3362221.25
Controllable Load that does NOT Need to be Reduced | 5653525.35 | 2523504.57 | 1517688.7525 | 1032893.775 | 1212602.435 | 1288739.3925 | 793294.8975
Reduction Needed from 2016 | 12044699.65 | 4304175.43 | 3031849.9975 | 2321057.225 | 2294056.065 | 889257.3575 | 1864218.8525
Loads Already Reduced as of 2016 | 6882320 | 4144079 | 2049108 | 1136891.5 | 1765526 | 3425218 | 791594.5
Tier 1 (First 25% of Reductions)
Tier 2 (Second 25% of Reductions)

## Slide 8
Existing Programs/Enhancements -- PROPOSED
Permitting, Compliance and Enforcement Initiatives
Agriculture-
  Manure Management
  Act 38
  Agriculture Erosion and Sediment Control
Stormwater-
  MS4s and PRPs
  Refinements in Next Permit Cycle
  Non-MS4 Communities
Wastewater-
  Existing Permit Caps
  Non-Significant Facilities
  ENR at Significant Facilities
  Septics
    Connections to Treatment Facilities
    Nutrient Treatment on on-lot Systems
Technical/Financial Assistance and Outreach
Agriculture –
  Soil Health (PA in the Balance)
  Expanded Nutrient Management
  Manure Treatment, Storage and Transportation
  Riparian Ecosystems
Stormwater-
  “Trees and Pollinators”
  Stream Restoration
Forestry (Sector Growth)
  Riparian/Forest Buffers
  Protected Lands/Land Conservation
    Agriculture and Forest
  Tree Canopy

## Slide 9
Local Initiatives
Potential progress with new and existing state agency programs
Reductions Already Made
Hypothetical journey to a county goal (nitrogen)
Permitting, Compliance and Enforcement Initiatives
Technical and Financial Assistance and Outreach Initiatives
Progress from 1985 through 2016
Level of Effort – Conceptual Framework
+
Customized Partnership by County

## Slide 10
Agriculture
  33,000 Farms, < 400 CAFOs or CAOs with a NPDES Permit
  All must comply with Manure Management and Agriculture Erosion and Control Plan Regulations
  Nitrogen Loading from Lancaster = Delaware + West Virginia + DC = New York = 21% of needed reduction for Pennsylvania
Urban Stormwater
  Nearly 75% of developed acres are outside of an MS4 or combined sewer system area.
  Existing Permitting and Compliance Programs cover very little of the urban sector’s contribution
Wastewater
  Met the required 2017 reduction goals 3 years early at a cost of $1.4 billion
  Are on track to meet the 2025 goals without further enhancements
Pennsylvania – Nonpoint Source Opportunities
Notes: There is a new focus in Pennsylvania on accomplishing local water quality and other local environmental restoration goals through the planning efforts of the Phase 3 WIP. There is very little low hanging fruit, so to speak, in Pennsylvania, since very little of our loads come from a source covered by a permit that can easily be established, monitored and enforced.
Wastewater was successful because:
Collaborative effort, enforceable goals were established and put into permits where compliance is easily measured and penalties taken accordingly.
Once goals were set, everyone was on board, it just becomes a matter of money … $1.4 billion to be exact.
We can do the same for nonpoint source:
Collaboration and partnerships are hard, but can be accomplished with established goals.
Once the goals are set, where is the money and resources going to come from?

## Slide 11
Chart: FY14-17 Average Funding by County Tiers
| Lancaster | York | Franklin | Lebanon | Cumberland | Dauphin | Centre | Bedford | Adams | Northumberland | Perry | Huntingdon | Columbia | Snyder | Mifflin | Lycoming | Schuylkill | Juniata | Union | Bradford | Chester | Clinton | Tioga | Susquehanna | Berks | Clearfield | Fulton | Blair | Lackawanna | Cambria | Montour | Luzerne | Sullivan | Potter | Wyoming | Somerset | Indiana | Elk | Cameron | Wayne
FY14-17 Average | 9471907.9862 | 3727482.4546 | 2549574.9766 | 1923140.2585 | 2771799.4791 | 2568465.2799 | 2763696.7112 | 1919679.7827 | 2418502.705 | 1697057.023 | 1144078.2178 | 1197759.506 | 1951739.1004 | 1142190.2954 | 1295229.8172 | 4042092.7612 | 2100726.6131 | 1690331.8162 | 1355717.7283 | 6837072.7065 | 9122229.7486 | 862373.8218 | 3518372.5631 | 5114820.6877 | 4521027.928 | 1632524.7001 | 849625.2015 | 1324071.2592 | 1216720.259 | 872602.0981 | 1422304.4425 | 2875360.7524 | 891990.25 | 1108330.8728 | 1569582.9343 | 626919.3207 | 909133.9133 | 530267.855 | 408319.1775 | 742571.1868

## Slide 12
Bay Program “Stacking” Efforts
  Brook Trout
  Climate Resiliency
  Fish Habitat
  Forest Buffers
  Healthy Watersheds
  Protected Lands
  Public Access
  Stream Health
  Submerged Aquatic Vegetation
  Toxic Contaminants
  Tree Canopy
  Wetlands

## Slide 13
Templates

## Slide 14
Countywide Plan Development -- Steps
Convene Countywide Action Team Members
Identify Water Quality and Other Goals
Identify Local Resources
Select and Report Actions
Implement Actions

## Slide 15
Countywide Plan Development – Resources
Support Team
  DEP Staff Person from Chesapeake Bay Office
  Member of Technical Support Team
  Members, as needed, of the Steering Committee Workgroups
County Planning Toolbox
  County Specific Data
  List of Resources and Contacts
  Community Outreach Tools
  Templates for Use in Completing the Action Plan

## Slide 16
Countywide Plan Development – Series of Meetings
May –
  Convening – Local Leaders Define Members and Process
June –
  Background and Information Gathering
  Identify Local Initiatives to Add
July/August –
  Define action steps and potential reductions
  Define Local Priorities
  Refine Scoping Scenarios
  Identify existing and needed resources
September –
  Draft Action Plan for Submittal to DEP by October
Implementation Team Meetings
  Follow Up Meetings as Needed as the Action Plan is Implemented

## Slide 17
Milestones and Progress (Outputs)
  BMP Verification Plan
  Tracking and Reporting
  Indicators of Progress
  “PA Barometer”

## Slide 18
Developing a toolbox for county stakeholders to use in determining locally how they will meet their goal
  Informed by sector-based work groups
  April 10 – Local Planning Process Kickoff
Countywide Planning Goals – May through October
  Pilot Process in 3 to 4 counties
Continued public engagement and input
  Fact Sheets, Program Updates, Website
  Forums, Regional Meetings – May through October 2018
  Public Review and Comment Period on Draft WIP Plan – March 2019
Final Phase 3 WIP – June 2019
Local Engagement --

## Slide 19
DEP Chesapeake Bay Program Website:
http://www.dep.pa.gov/ChesapeakeBay
Phase 3 WIP Website:
www.dep.pa.gov/chesapeakebay/phase3
Contact Information:
Veronica Kasi
vbkasi@pa.gov
717-772-4053