## Slide 1: Landuse
Fairfax County, Virginia
Watershed Management Plans

## Slide 2: Scope of task
Develop countywide land use/ land cover GIS data layers useful for plan development
  Watershed characterization (i.e. maps, data analysis)
  Pollution & Hydrologic modeling
Key requirements:
  A layer containing a land use mix for both existing and future conditions
    Key parameter for modeling water quality
  A layer containing Impervious values (connected & disconnected) for both conditions
    Key parameter for modeling water quantity

## Slide 3: Available digital data
Tax Administration real estate records
  Each record contained a unique code for each parcel:
    Existing land use
    Zoned land use
Adopted land use comprehensive plan
  Polygons containing planned land use information
  Twenty-two different planned land use categories
Parcel data
  Polygons contained a unique ID for each parcel
  Included vacant & underutilized parcels
Planimetric data (1997 aerial photography)
Codes > 200 types

## Slide 4: Consolidation
The need to simplify (i.e. group) land use types through consolidation was evident
  200 different codes (included embedded towns)
  Code numbering convention facilitated consolidation

## Slide 5: Consolidation
  Residential:
    ESR - Estate > 2 acres/residence
    LDR - Low Density ½ - 2 acres/residence
    MDR - Medium Density < ½ acre/residence < 8 dwellings/acre
    HDR - High Density < acre/residence
  Commercial:
    LIC - Low Intensity
    HIC - High Intensity
  Miscellaneous:
    OS - Open Space
    GC - Golf Course
    INT - Institutional:
      Government/Universities
    IND - Industrial
      Airports
      Railways
  Transportation:
    TRANS - Road rights-of-way
Grouped existing, zoned & planned land use types into 11 categories:

## Slide 6: Creating landuse layer - a GIS exercise
Existing conditions:
Each real estate record was assigned a category for existing, zoned & planned land use
Joined the tabular tax record data to the parcel layer polygons
Included category: TRANS landuse
  Areas outside of the parcel boundaries = ROW
Included category: WATER land cover
  Planimetric data of the stream network, lakes

## Slide 7: Creating landuse layer - a GIS exercise
Future conditions:
Intersected comprehensive plan coverage with the parcel layer
  Most parcels were already built-out
Vacant & underutilized parcels
  Compared zoned vs. planned land use
  Where different, chose classification that yielded the greatest density

## Slide 8: Creating landuse layer - a GIS exercise
Existing conditions - Tysons Corner

## Slide 9: Creating landuse layer - a GIS exercise
Future conditions - Tysons Corner
future

## Slide 10: Estimating imperviousness values
Used planimetric data
  Features were assigned a corresponding % imperviousness
    Buildings, roads, parking lots & sidewalks/trails – 100%
    Parking lots, unpaved – 50%
    Areas outside planimetric features – 0%
Feature types sampled to estimate the typical DCIA/NDCIA split
  Roads, parking lots – 100% DCIA
  Sidewalks/trails – 85% DCIA, 15% NDCIA
  Buildings – DCIA varied by type
    Commercial - 100%
    Industrial - 95%
    Multi-Family Residential - 90%
    Single Family Residential - 50%

## Slide 11: Estimating imperviousness values
Planimetrics - Tysons Corner

## Slide 12: Estimating imperviousness values
Estimating exist & future condition imperviousness values by land use:
  Sampled planimetric data in areas representative for each land use category
  Average % imperviousness was calculated for each land use category
  Assigned % DCIA/NDCIA to each category based on appropriate feature types
DCIA & NDCIA values were aggregated to a “subbasin” level
  Polygons were created for modeling purposes
  Typically 300-500 acres in size
  Over 1800 polygons

## Slide 13: Estimating imperviousness values
Existing % Imperv by Land use - Tysons Corner

## Slide 14: Estimating imperviousness values
Future % Imperv by Land use - Tysons Corner

## Slide 15: Conclusion/Challenges
The LU/LC methodology Fairfax County implemented for its watershed planning effort worked well at the local scale & could be a method used to help standardize urbanized LU/LC categories across the bay watershed.
Many smaller jurisdictions have less readily available data, however; many larger urban areas maintain data similar to Fairfax (i.e. comp plan, tax/parcel information & planimetrics) which could be used with this methodology.

## Slide 16
Questions?