## Slide 1: The Law-borist
Enforcing the District of Columbia’s Municipal Tree Law

## Slide 2: Urban Forestry Division, Washington D.C.
20 arborists, 4 teams
District Department of Transportation (DDOT)
675,000 people
150,000 street trees
61 sq. mi.

## Slide 3: D.C.: The City of Trees
40% Canopy Goal by 2032
Plant 8,000 Trees a Year
Issue Tree Removal Permits

## Slide 4: Urban Forest Preservation Act of 2002 (plus 2016 Amendment)
Undersized < 44”
44” < Special > 100”
100” < Heritage Trees

## Slide 5: Urban Forest Preservation Act of 2002 (plus 2016 Amendment)
$55 per inch of circumference to remove non-hazardous trees.
$300 per inch of circumference fine for illegal removals.
Trees measured at 4.5 feet above the ground

## Slide 6: Case Study #1: The Gainesville Case

## Slide 8: Burden of Proof
Civil Trial
  Preponderance of the Evidence
    Was the respondent more likely than not to have committed the infraction?
Criminal Trial
  Beyond a Reasonable Doubt
    Is there a reasonable doubt the defendant committed the crime?

## Slide 9: Burden of Proof
Civil Trial
  Preponderance of the Evidence
    Was the respondent more likely than not to have committed the infraction?
Criminal Trial
  Beyond a Reasonable Doubt
    Is there a reasonable doubt the defendant committed the crime?

## Slide 10: Two Parcels

## Slide 11: Property Boundary Staked

## Slide 12: Stump Grinding

## Slide 13: Burden of Proof
Civil Trial
  Preponderance of the Evidence
    Was the respondent more likely than not to have committed the infraction?
Criminal Trial
  Beyond a Reasonable Doubt
    Is there a reasonable doubt the defendant committed the crime?

## Slide 14: What do we measure???

## Slide 15: What information do we have?
Stump D
Stump H
Species
Total tree height, using LIDAR

## Slide 16: Measuring TH with LIDAR

## Slide 17: ORMEROD EQUATION:* D^2/DBH^2 = [(TH – H) / (TH – 4.5)]^2b1
Where . . .
  D = the measured diameter
  H = height of the measured diameter
  TH = total height of the tree (obtained from LIDAR data)
  DBH = diameter at breast height
  b1 = species-specific co-efficient developed by USFS
  *Martin, A. Jeff. “Taper and Volume Equations for Selected Appalachian Hardwood Species.” United States Department of Agriculture. 1981.

## Slide 18: In Excel . . .
Solve for DBH
=SQRT(D^2/((TH-H)/TH-4.5))^(2*b1)

## Slide 19: Tree Fines

## Slide 20: Total Fine: $114,740.07

## Slide 21: Case Study #2: The Robinson Case

## Slide 22: Evidence

## Slide 23: Ouch Emoji

## Slide 24: Judges Can Suspend Fines . . .
(1) Past Compliance
(2) Past Good Faith Attempts to Comply with Applicable Laws and Regulations
(3) Respondent Correct the Infraction by a Date Certain

## Slide 25: Best Case
“Respondent has accepted responsibility . . .”
“Respondent was properly permitted and paid the fees . . . for the Special Trees . . .”
“. . . This Heritage Tree is barely over the threshold to qualify as a Heritage Tree . . .”

## Slide 26: Best Case
“Respondent has accepted responsibility . . .”
“Respondent was properly permitted and paid the fees . . . for the Special Trees . . .”
“. . . This Heritage Tree is barely over the threshold to qualify as a Heritage Tree . . .”
$31,197  $18,000

## Slide 27: Fine Reductions
2014-DDOT-U100115
  $21,823.00  $5,000
  “. . . a first-time offense . . .”
2014-DDOT-U100066
  $8,765.00  $3,067.75
  “. . . Respondent acted in good faith by applying for the permit . . .”

## Slide 28: Canopy = 38.5%

## Slide 29: Contact
John O’Neill
Urban Forester, Ward 8 District of Columbia Government
john.oneill@dc.gov
(202) 527- 5633