## Slide 1
Chesapeake Bay Program Principals’ Staff Committee December 19, 2017
Chesapeake Bay 2017 Midpoint Assessment— Policy Issues for Partnership Decisions

## Slide 2
Overview of Meeting and Policy Decision Recommendations
Teresa Koon, WV DEP, CBP Water Quality Goal
Implementation Team Vice Chair

## Slide 3: Day 1 Requested PSC Decisions
Adoption of the Phase 6 suite of modeling tools for finalizing the draft Phase III planning targets and for management application in the Phase III WIPs and two-year milestones through 2025
Approval of the proposed Bay’s assimilative capacity
Approval of the process for the 4-month Partnership review of the draft Phase III WIP planning targets, including how special cases are addressed
Base Phase III WIP development on 2025 current zoning conditions

## Slide 4: Day 2 Requested PSC Decisions
Develop a Partnership implementation plan to address Conowingo infill
Adopt a dual approach to factor climate change into the Phase III WIPs
Approval of the draft Phase III WIP planning targets as a starting point of the 4-month Partnership review period

## Slide 5: Overview of PSC Meeting
Today
Focus on building understanding and answering questions
Focus on consensus building and collaborative decision-making on foundational midpoint assessment issues
Opportunity for evening jurisdictional caucuses
Tomorrow
Focus on consensus building and collaborative decision-making on key policy issues

## Slide 6
Jurisdiction | 1985 Baseline | 2013 Progress | Growth in Load to 2025 | Phase III Planning Target
NY | 18.71 | 15.44 | -0.74 | 10.59
PA | 122.41 | 99.28 | 1.66 | 73.18
MD | 83.56 | 55.89 | 1.52 | 45.30
WV | 8.73 | 8.06 | -0.02 | 6.35
DC | 6.48 | 1.75 | 0.00 | 2.43
DE | 6.97 | 6.59 | 0.48 | 4.59
VA | 84.29 | 61.53 | 1.09 | 55.82
Basinwide | 331.15 | 248.54 | 4.00 | 198.25
*Units: millions of pounds
WQGIT & Modeling Workgroup Recommendations: Nitrogen

## Slide 7
Jurisdiction | 1985 Baseline | 2013 Progress | Growth in Load to 2025 | Phase III Planning Target
NY | 1.198 | 0.710 | -0.005 | 0.506
PA | 6.115 | 3.696 | 0.044 | 3.073
MD | 7.419 | 3.919 | -0.015 | 3.604
WV | 0.793 | 0.560 | -0.017 | 0.456
DC | 0.090 | 0.062 | 0.000 | 0.130
DE | 0.225 | 0.115 | 0.007 | 0.120
VA | 13.545 | 6.345 | 0.140 | 6.186
Basinwide | 29.384 | 15.408 | 0.154 | 14.073
*Units: millions of pounds
WQGIT & Modeling Workgroup Recommendations: Phosphorus

## Slide 10: Cautions About Comparisons Back to Phase II WIPs
Be cautious with comparing the proposed draft Phase III planning targets with the jurisdictions’ Phase II WIP loads
  Different watershed models – more BMPs, different land uses and loading rates
  State-driven changes between Phase II and Phase III
  Phase II WIP planning targets were not derived using the Bay TMDL allocation methodology—they were based on a similar level of effort to the Phase I WIPs

## Slide 11
What’s Changed,
the Implications, and
Our Improved Models
Lee Currey, MDE, CBP Modeling Workgroup Co-Chair

## Slide 12: What’s Changed, Why, and Implications
A lot has changed since 2010 and our Phase I and Phase II WIPs
  Much improved modeling and other decision support tools
  High resolution land cover data for entire watershed
  Hundreds more BMPs available for crediting
  Significant data gathered from local agricultural and municipality partners incorporated into our models and other decision support tools

## Slide 13: Improved Partnership Models
5 years of collaborative Partnership decision-making on every aspect of every model
Multiple STAC-sponsored technical workshops from soil phosphorus to Conowingo
Independent scientific peer reviews of every Partnership model
Comprehensive fatal flaw review and issue resolution by the partners

## Slide 14: Phase 6 Bay Watershed Model
Average Load + Inputs * Sensitivity
Land Use Acres
BMPs
Land to Water
Stream Delivery
River Delivery
Direct Loads
Phase 6 Watershed Model
Prior Bay Watershed Models
*
*
*
*
*

## Slide 15
Phase 5
30-Meter Resolution Land Use/Land Cover Data
Phase 6
1-Meter Resolution Land Use/Land Cover Data

## Slide 16: Hundreds More BMPs

## Slide 17: Local Agricultural and Municipality Data
Municipal Separate Storm Sewer Systems
Combined Sewer Systems
Sewer Service Areas
Land Cover
Land Use
Parcels
Roads
Beaches
Institutional lands
Federal lands
Golf courses
Surface mines
Landfills
Protected lands
Streams
Wetlands
Tidal zones
Floodplains
Frequently flooded soils
Livestock populations
Poultry populations
Crop, hay and pasture acreages
Crop yields
Soil P concentrations
BMPs

## Slide 18
Our Models are Tested using Decades of Monitoring Data
Hundreds of thousands of water quality monitoring data points
Hundreds of monitoring stations
Nitrogen, phosphorus, and sediment
Data records lasting up to 3 decades
Size of circle denotes relative number of data points: 100s to 1,000s

## Slide 19
[1] Model calibration is made to improve agreement with monitoring data
[2] Simulated vs. WRTDS Per Acre Load and the Geographic Efficiencies
[3] Simulated vs. WRTDS loads
[4] Agreement between the simulated and WRTDS loads at the RIM sites
Extensive Testing of the
Models Throughout the Watershed

## Slide 20
Best Match with Monitoring Data Ever!
NSE of monthly phosphorus load
NSE of annual phosphorus loads
= 0.942
= 0.935
Conowingo Phase 6 Simulation Compared to Annual WRTDS Loads

## Slide 21
Best Match with Monitoring Data Ever!
NSE of monthly phosphorus load
NSE of annual phosphorus loads
= 0.942
= 0.935
Conowingo Phase 6 Simulation Compared to Monthly WRTDS Loads

## Slide 22: Today’s Requested Policy Decision
Adoption of the Phase 6 suite of modeling tools for finalizing the Phase III planning targets and for management application in the Phase III WIPs and two-year milestones through 2025

## Slide 23
Phase III WIP Planning Targets Methodology
Gary Shenk, USGS, CBP Phase 6 Watershed Model Coordinator

## Slide 24: Review of the Phase III Planning Targets Methodology
A step by step walk through of the agreed-to Phase III planning targets methodology
How it works to allocate updated cap loads equitably among the jurisdictions

## Slide 25: Three Partnership Principals
Allocated loads must result in achievement of the states’ Bay water quality standards
Major river basins that contribute the most to Bay water quality problems must do the most to resolve those problems
All tracked and reported reductions in loads are credited toward achieving assigned loads
Source: 2010 Chesapeake Bay TMDL

## Slide 26: More Impact, Do More
Phase 5 Nitrogen Nitrogen
Phase 6 Nitrogen

## Slide 27: More Impact, Do More
Phase 5 Phosphorus
Phase 6 Phosphorus

## Slide 28: Defining the Controllable Load
No Action
E3
Controllable Load
No Action:
Watershed conditions with minimal to no controls on load
Wastewater at primary treatment
E3 or “Everything by Everyone, Everywhere”:
Watershed conditions with maximum controls on loads, regardless of cost
Wastewater at high level of nutrient control
  3mg/l TN, 0.1 mg/l TP

## Slide 29
Determining the Bay’s Ability to Absorb Pollutants

## Slide 30: Allowing for Special Cases
Previously agreed to consider special cases put forth by jurisdictions
Consideration of special cases factored into four-month review process
CBPO will provide support to jurisdictions considering special cases
Final decisions on allowance of special cases will be made by the PSC in April 2018

## Slide 31: Nitrogen and Phosphorus Exchanges
Science supports exchanges in nitrogen and phosphorus load reductions
Better science has resulted in changes to our existing exchange ratios
  Better simulation of observed nutrient limitation in the Bay
  Inclusion of new P sources from Conowingo and Shoreline makes each pound of P less important
Phase 5
Phase 6
Nitrogen for Phosphorus: 5 1.34 – 3.84
Phosphorus for Nitrogen: 0.067 0.26 – 0.75

## Slide 32: Accounting for Nitrogen Air Deposition to Bay Watershed
Updated estimated benefits to Bay and watershed from clear air actions.
From 1985 through 2025, the jurisdictions will receive an estimated 254 million lbs. less nitrogen on their lands and rivers.

## Slide 33: Accounting for Nitrogen Air Deposition to Bay Tidal Waters
From 1985 through 2025, loads will be reduced from 21.5 to 15.6 million lbs.
By 2025, 0.1 million pounds below EPA’s Bay TMDL allocation (15.7 million lbs.)
By 2030, load drops to 14.9 millions lbs., 0.8 million pounds below EPA’s Bay TMDL allocation

## Slide 34
Determining the Bay’s Ability to Absorb Pollutants
(Assimilative Capacity)
Rich Batiuk, U.S. EPA CBPO Associate Director for Science, Analysis and Implementation

## Slide 35
Here’s Where We Want to Get to

## Slide 36
What’s Changed and the Implications
An improved Water Quality and Sediment Transport Model (WQSTM) is providing a better simulation of dissolved oxygen in the tidal Bay affording higher confidence in implementation planning for 2025.
Good simulation of DO concentrations of Open Water, Deep Water, and Deep Channel (CB4 shown here)

## Slide 37: What’s Changed and the Implications
The Chesapeake Bay’s summertime dead zone is decreasing in size!
Source: Testa et al. 2017

## Slide 38: What Hasn’t Changed
  Delaware, District of Columbia, Maryland and Virginia’s Chesapeake Bay water quality standards regulations have not changed since 2012
    Five tidal habitat-based designated uses
    Dissolved oxygen, SAV, water clarity and chlorophyll a criteria to protect those uses
    Fully consistent criteria attainment assessment procedures
    How we use model output to assess criteria attainment under model-simulated load conditions

## Slide 39
Maryland’s water quality standards regulations still contain restoration variances agreed to by the Partners/approved by EPA in 2010 and updated in 2012
Maryland’s Restoration Variances
Patapsco River Deep-water 7%
Lower Chester River Deep-channel 16%
Eastern Bay Deep-channel 2%
Middle Central Chesapeake Bay
  Deep-water 7%
  Deep-channel 2%

## Slide 40
ANATF_DC
ANATF_MD
PISTF
POTOH1_MD
POTOMH_MD
PMKOH
YRKMH
YRKPH
Segments Attaining Oxygen Standards: Open-Water Use
No Action
404 TN 41.7 TP
E3
All Forest
ELIPH
C&Dcanal
ELKOH
SASOH
EASMH
CHOTF
CHOOH
CHOMH2
CHOMH1
POCTF
POCOH_MD
POCOH_VA
TANMH_VA
CB2OH
CB6PH
CB7PH
BSHOH
SEVMH
PAXOH
PAXMH
POTTF_DC
POTTF_MD
Segments NOT in Attainment

## Slide 41
Segments Attaining Oxygen Standards: Open-Water Use
347 TN 30.4 TP
E3
All Forest
CB6PH
CB7PH
PAXOH
PAXMH
ANATF_DC
ANATF_MD
PISTF
POTOH1_MD
YRKMH
YRKPH
C&Dcanal
SASOH
CHOMH2
CHOMH1
POCTF
POCOH_MD
POCOH_VA
TANMH_VA
Segments NOT in Attainment

## Slide 42
Segments Attaining Oxygen Standards: Open-Water Use
E3
All Forest
CB6PH
CB7PH
PAXOH
PAXMH
ANATF_DC
ANATF_MD
PISTF
POTOH1_MD
YRKMH
YRKPH
C&Dcanal
SASOH
CHOMH2
CHOMH1
POCTF
POCOH_MD
POCOH_VA
TANMH_VA
Segments NOT in Attainment
337 TN
23.7 TP

## Slide 43
Segments Attaining Oxygen Standards: Open-Water Use
337 TN
23.7 TP
E3
All Forest
CB6PH
CB7PH
WSTMH
PAXOH
PAXMH
ANATF_DC
ANATF_MD
PISTF
YRKMH
YRKPH
SASOH
CHOMH2
CHOMH1
TANMH_VA
Segments NOT in Attainment

## Slide 44
Segments Attaining Oxygen Standards: Open-Water Use
317 TN 21.9 TP
E3
All Forest
CB6PH
CB7PH
PAXOH
ANATF_DC
ANATF_MD
PISTF
YRKMH
SASOH
CHOMH2
POCTF
POCOH_MD
POCOH_VA
Segments NOT in Attainment

## Slide 45
Segments Attaining Oxygen Standards: Open-Water Use
E3
All Forest
CB6PH
CB7PH
PAXOH
ANATF_DC
ANATF_MD
PISTF
YRKMH
SASOH
CHOMH2
POCTF
POCOH_MD
POCOH_VA
Segments NOT in Attainment
266 TN 16.9 TP

## Slide 46
Segments Attaining Oxygen Standards: Open-Water Use
253 TN 15.9 TP
E3
All Forest
CB7PH
ANATF_DC
ANATF_MD
PISTF
YRKMH
CHKOH
Segments NOT in Attainment

## Slide 47
Segments Attaining Oxygen Standards: Open-Water Use
224 TN 14.8 TP
E3
All Forest
PAXOH
ANATF_DC
ANATF_MD
PISTF
YRKMH
Segments NOT in Attainment

## Slide 48
Segments Attaining Oxygen Standards: Open-Water Use
205 TN 14.0 TP
E3
All Forest
ANATF_MD
YRKMH
Segments NOT in Attainment

## Slide 49
Segments Attaining Oxygen Standards: Open-Water Use
195 TN 13.7 TP
E3
All Forest
Segments NOT in Attainment

## Slide 50
Segments Attaining Oxygen Standards: Open-Water Use
185 TN 12.8 TP
E3
All Forest
Segments NOT in Attainment

## Slide 51
Segments Attaining Oxygen Standards: Open-Water Use
174 TN 11.9 TP
E3
All Forest
Segments NOT in Attainment

## Slide 52
Segments Attaining Oxygen Standards: Open-Water Use
133 TN
8.6 TP
E3
All Forest
Segments NOT in Attainment

## Slide 53
Segments Attaining Oxygen Standards: Open-Water Use
All Forest
40 TN
3.9 TP
E3
Segments NOT in Attainment

## Slide 54
Segments Attaining Oxygen Standards:
Open-Water Use

## Slide 55
Segments Attaining Oxygen Standards: Deep-Water Use
No Action
404 TN 41.7 TP
E3
All Forest
CB3MH
CB4MH
CB5MH_MD
PATMH
MAGMH
SEVMH
PAXMH
POTMH
RPPMH
CHSMH
EASMH
Segments NOT in Attainment

## Slide 56
Segments Attaining Oxygen Standards: Deep-Water Use
347 TN 30.4 TP
E3
All Forest
CB3MH
CB4MH
CB5MH_MD
PATMH
MAGMH
SEVMH
PAXMH
POTMH
RPPMH
CHSMH
EASMH
Segments NOT in Attainment

## Slide 57
Segments Attaining Oxygen Standards: Deep-Water Use
E3
All Forest
CB3MH
CB4MH
CB5MH_MD
PATMH
MAGMH
SEVMH
PAXMH
POTMH
RPPMH
CHSMH
EASMH
Segments NOT in Attainment
338 TN 27.7 TP

## Slide 58
Segments Attaining Oxygen Standards: Deep-Water Use
337 TN
23.7 TP
E3
All Forest
CB4MH
CB5MH_MD
PATMH
MAGMH
SEVMH
PAXMH
POTMH
RPPMH
CHSMH
EASMH
Segments NOT in Attainment

## Slide 59
Segments Attaining Oxygen Standards: Deep-Water Use
317 TN 21.9 TP
E3
All Forest
CB4MH
CB5MH_MD
PATMH
MAGMH
PAXMH
POTMH
RPPMH
CHSMH
Segments NOT in Attainment

## Slide 60
Segments Attaining Oxygen Standards: Deep-Water Use
E3
All Forest
Segments NOT in Attainment
317 TN 21.9 TP
CB4MH
CB5MH_MD
MAGMH
RPPMH

## Slide 61
Segments Attaining Oxygen Standards: Deep-Water Use
253 TN 15.9 TP
E3
All Forest
CB4MH
CB5MH_MD
MAGMH
RPPMH
Segments NOT in Attainment

## Slide 62
Segments Attaining Oxygen Standards: Deep-Water Use
224 TN 14.8 TP
E3
All Forest
CB5MH_MD
MAGMH
Segments NOT in Attainment

## Slide 63
Segments Attaining Oxygen Standards: Deep-Water Use
205 TN 14.0 TP
E3
All Forest
MAGMH
Segments NOT in Attainment

## Slide 64
Segments Attaining Oxygen Standards: Deep-Water Use
195 TN 13.7 TP
E3
All Forest
Segments NOT in Attainment

## Slide 65
Segments Attaining Oxygen Standards: Deep-Water Use
185 TN 12.8 TP
E3
All Forest
Segments NOT in Attainment

## Slide 66
Segments Attaining Oxygen Standards: Deep-Water Use
174 TN 11.9 TP
E3
All Forest
Segments NOT in Attainment

## Slide 67
Segments Attaining Oxygen Standards: Deep-Water Use
E3
All Forest
133 TN
8.6 TP
Segments NOT in Attainment

## Slide 68
Segments Attaining Oxygen Standards: Deep-Water Use
All
Forest
40 TN
3.9 TP
E3
Segments NOT in Attainment

## Slide 69
Segments Attaining Oxygen Standards:
Deep-Water Use

## Slide 70
Segments Attaining Oxygen Standards: Deep-Channel Use
No Action
404 TN 41.7 TP
Count: X of YY
For this first animation, include all deep-channel segments, even the greyed out problem segments so when we get to the Phase II WIP loads (and beyond), we want to show the WQGIT these specific remaining segments. The last slide in this animation needs to circle the problem segments on the graphic—those same problem segments will remain listed in the bulleted listing to the left.
CB3MH
CB4MH
CB5MH_MD
CB5MH_VA
PATMH
POTMH
RPPMH
CHSMH
E3
All Forest
Segments NOT in Attainment

## Slide 71
Segments Attaining Oxygen Standards: Deep-Channel Use
347 TN 30.4 TP
Count: X of YY
For this first animation, include all deep-channel segments, even the greyed out problem segments so when we get to the Phase II WIP loads (and beyond), we want to show the WQGIT these specific remaining segments. The last slide in this animation needs to circle the problem segments on the graphic—those same problem segments will remain listed in the bulleted listing to the left.
CB3MH
CB4MH
CB5MH_MD
CB5MH_VA
PATMH
POTMH
RPPMH
CHSMH
E3
All Forest
Segments NOT in Attainment

## Slide 72
Segments Attaining Oxygen Standards: Deep-Channel Use
Count: X of YY
For this first animation, include all deep-channel segments, even the greyed out problem segments so when we get to the Phase II WIP loads (and beyond), we want to show the WQGIT these specific remaining segments. The last slide in this animation needs to circle the problem segments on the graphic—those same problem segments will remain listed in the bulleted listing to the left.
CB3MH
CB4MH
CB5MH_MD
CB5MH_VA
PATMH
POTMH
RPPMH
CHSMH
E3
All Forest
Segments NOT in Attainment
338 TN 27.7 TP

## Slide 73
Segments Attaining Oxygen Standards: Deep-Channel Use
Count: X of YY
For this first animation, include all deep-channel segments, even the greyed out problem segments so when we get to the Phase II WIP loads (and beyond), we want to show the WQGIT these specific remaining segments. The last slide in this animation needs to circle the problem segments on the graphic—those same problem segments will remain listed in the bulleted listing to the left.
337 TN
23.7 TP
CB3MH
CB4MH
CB5MH_MD
CB5MH_VA
POTMH
RPPMH
CHSMH
E3
All Forest
Segments NOT in Attainment

## Slide 74
Segments Attaining Oxygen Standards: Deep-Channel Use
317 TN 21.9 TP
Count: X of YY
For this first animation, include all deep-channel segments, even the greyed out problem segments so when we get to the Phase II WIP loads (and beyond), we want to show the WQGIT these specific remaining segments. The last slide in this animation needs to circle the problem segments on the graphic—those same problem segments will remain listed in the bulleted listing to the left.
E3
All Forest
Segments NOT in Attainment
CB3MH
CB4MH
CB5MH_MD
CHSMH
POTMH
RPPMH

## Slide 75
Segments Attaining Oxygen Standards: Deep-Channel Use
253 TN 15.9 TP
E3
All Forest
CB4MH
CB5MH_MD
For this first animation, include all deep-channel segments, even the greyed out problem segments so when we get to the Phase II WIP loads (and beyond), we want to show the WQGIT these specific remaining segments. The last slide in this animation needs to circle the problem segments on the graphic—those same problem segments will remain listed in the bulleted listing to the left.
Segments NOT in Attainment

## Slide 76
Segments Attaining Oxygen Standards: Deep-Channel Use
224 TN 14.8 TP
Count: X of YY
For this first animation, include all deep-channel segments, even the greyed out problem segments so when we get to the Phase II WIP loads (and beyond), we want to show the WQGIT these specific remaining segments. The last slide in this animation needs to circle the problem segments on the graphic—those same problem segments will remain listed in the bulleted listing to the left.
CB4MH
E3
All Forest
Segments NOT in Attainment

## Slide 77
Segments Attaining Oxygen Standards: Deep-Channel Use
205 TN 14.0 TP
Count: X of YY
For this first animation, include all deep-channel segments, even the greyed out problem segments so when we get to the Phase II WIP loads (and beyond), we want to show the WQGIT these specific remaining segments. The last slide in this animation needs to circle the problem segments on the graphic—those same problem segments will remain listed in the bulleted listing to the left.
CB4MH
E3
All Forest
Segments NOT in Attainment

## Slide 78
Segments Attaining Oxygen Standards: Deep-Channel Use
195 TN 13.7 TP
Count: X of YY
For this first animation, include all deep-channel segments, even the greyed out problem segments so when we get to the Phase II WIP loads (and beyond), we want to show the WQGIT these specific remaining segments. The last slide in this animation needs to circle the problem segments on the graphic—those same problem segments will remain listed in the bulleted listing to the left.
CB4MH
E3
All Forest
Segments NOT in Attainment

## Slide 79
Segments Attaining Oxygen Standards: Deep-Channel Use
185 TN 12.8 TP
Count: X of YY
For this first animation, include all deep-channel segments, even the greyed out problem segments so when we get to the Phase II WIP loads (and beyond), we want to show the WQGIT these specific remaining segments. The last slide in this animation needs to circle the problem segments on the graphic—those same problem segments will remain listed in the bulleted listing to the left.
CB4MH
E3
All Forest
Segments NOT in Attainment

## Slide 80
Segments Attaining Oxygen Standards: Deep-Channel Use
174 TN 11.9 TP
E3
All Forest
Segments NOT in Attainment
Notes: For this first animation, include all deep-channel segments, even the greyed out problem segments so when we get to the Phase II WIP loads (and beyond), we want to show the WQGIT these specific remaining segments. The last slide in this animation needs to circle the problem segments on the graphic—those same problem segments will remain listed in the bulleted listing to the left.

## Slide 81
Segments Attaining Oxygen Standards: Deep-Channel Use
133 TN
8.6 TP
E3
All Forest
Segments NOT in Attainment

## Slide 82
Segments Attaining Oxygen Standards: Deep-Channel Use
All
Forest
40 TN
3.9 TP
E3
Segments NOT in Attainment

## Slide 83
Segments Attaining Oxygen Standards:
Deep-Channel Use

## Slide 84
Determining the Bay’s Ability to Absorb Pollutants

## Slide 85: Rationale for Pollutant Loads Bay Can Absorb
Clear monitoring-based evidence of reductions on volumes of low/no oxygen in deeper waters observed in Bay and tidal tributaries
At 195 million lbs. nitrogen and 13.7 million lbs. phosphorus, we reach:
  Loading levels where all segments’ designated uses, except CB4 deep-channel, come into attainment
  Point of diminishing returns for the increased level of reductions approaching E3

## Slide 86
Diminishing Return for Additional Reductions
Scoping Scenarios to explore water quality attainment at loads around 195N and 13.7P
+10M lbs TN
+19M lbs TN
- 9M lbs TN
-21M lbs TN

## Slide 87: Proposed Path Forward
Support Maryland updating their water quality standards regulations’ existing restoration variances
  Change CB4 deep-channel from 2 percent to 6 percent
  Change CB4 deep-water from 7 percent to 5 percent
  No change to the Eastern Bay restoration variance of 2 percent
  Remove the lower Chester River deep-channel restoration variance of 16 percent
  Remove the Patapsco River deep-water restoration variance of 7 percent

## Slide 88: Proposed Path Forward
Agreement to a common set of Partnership communication messages
  Reflects application of an additional decade of new data and scientific understanding along with improved models
  Approach followed is fully consistent with approach taken during development of the 2010 Bay TMDL
  Fully consistent with Maryland’s existing water quality standards regulations requirement for regular check-ins and modifications based on new data or assumptions incorporated into the Partnership’s Chesapeake Bay water quality model

## Slide 89: WQGIT Recommendations to the PSC
Recommends establishing the Bay’s assimilative capacity as 195 million pounds of nitrogen and 13.7 million pounds of phosphorus
Recommends supporting necessary adjustments to Maryland's water quality standards regulations’ restoration variances (subject to EPA approval) in order to meet the assimilative capacity for nitrogen and phosphorus
Recommends the development of Partnership communication messages for the public over the next four months, in time for the release of the final Phase III WIP planning targets in May 2018

## Slide 90: Today’s Requested Policy Decisions
Approval of the Bay’s assimilative capacity as 195 million pounds of nitrogen and 13.7 million pounds of phosphorus
Support the necessary adjustments to Maryland’s restoration variances
Approval for the development of the Partnership’s public communication messages

## Slide 91
Proposed Draft Phase III Planning Targets
Gary Shenk, USGS, CBP Phase 6 Watershed Model Coordinator
Notes: Centered text

## Slide 92: We Have All the Needed Components
Agreed-to methodology
No Action scenario
E3 scenario
Watershed and estuarine relative effectiveness
Assimilative capacity of the Bay
Accounting for projected atmospheric deposition load reductions

## Slide 93: Deriving the Draft Phase III Planning Targets: Nitrogen

## Slide 94: Deriving the Draft Phase III Planning Targets: Phosphorus

## Slide 95
Jurisdiction | 1985 Baseline | 2013 Progress | Growth in Load to 2025 | Phase III Planning Target
NY | 18.71 | 15.44 |  | 10.59
PA | 122.41 | 99.28 |  | 73.18
MD | 83.56 | 55.89 |  | 45.30
WV | 8.73 | 8.06 |  | 6.35
DC | 6.48 | 1.75 |  | 2.43
DE | 6.97 | 6.59 |  | 4.59
VA | 84.29 | 61.53 |  | 55.82
Basinwide | 331.15 | 248.54 |  | 198.25
Proposed Draft Phase III Planning Targets: Nitrogen
*Units: millions of pounds

## Slide 96
Jurisdiction | Special Cases | With Special Cases | Phase III Planning Target
NY | 1.00 | 11.59 | 10.59
PA | -0.58 | 72.60 | 73.18
MD | -0.31 | 44.99 | 45.30
WV | -0.03 | 6.31 | 6.35
DC | 0.00 | 2.42 | 2.43
DE | -0.06 | 4.53 | 4.59
VA | -0.24 | 55.58 | 55.82
Basinwide | -0.22 | 198.03 | 198.25
Proposed Draft Phase III Planning Targets with Special Cases: Nitrogen
*Units: millions of pounds

## Slide 97
Jurisdiction | 1985 Baseline | 2013 Progress | Growth in Load to 2025 | Phase III Planning Target
NY | 1.198 | 0.710 |  | 0.506
PA | 6.115 | 3.696 |  | 3.073
MD | 7.419 | 3.919 |  | 3.604
WV | 0.793 | 0.560 |  | 0.456
DC | 0.090 | 0.062 |  | 0.130
DE | 0.225 | 0.115 |  | 0.120
VA | 13.545 | 6.345 |  | 6.186
Basinwide | 29.384 | 15.408 |  | 14.073
Proposed Draft Phase III Planning Targets: Phosphorus
*Units: millions of pounds

## Slide 98
Jurisdiction | Special Cases | With Special Cases | Phase III Planning Target
NY | 0.100 | 0.606 | 0.506
PA | -0.102 | 2.971 | 3.073
MD | -0.083 | 3.521 | 3.604
WV | 0.200 | 0.656 | 0.456
DC | -0.001 | 0.129 | 0.130
DE | -0.004 | 0.115 | 0.120
VA | -0.133 | 6.053 | 6.186
Basinwide | -0.023 | 14.05 | 14.073
Proposed Draft Phase III Planning Targets with Special Cases: Phosphorus
*Units: millions of pounds

## Slide 101
Jurisdiction-Specific Proposed Draft Phase III WIP Planning Targets
Teresa Koon, WV DEP CBP Water Quality Goal
Implementation Team Vice Chair
and
WQGIT Jurisdictional Representations

## Slide 102: Draft Phase III Planning Targets
WQGIT jurisdictional representatives will present their respective profiles to the PSC

## Slide 103: Day Two Requested Policy Decision
Approval of draft Phase III Planning Targets as the starting point for the Partnership’s 4-month review process

## Slide 104
Proposed Process and Schedule for 4-Month Review Period
Lucinda Power, U.S. EPA, CBP Water Quality Goal
Implementation Team Coordinator

## Slide 105: PSC Approved Schedule
December 19-20, 2017: PSC 2-day retreat and decision making
December 22, 2017: Release of draft Phase III WIP planning targets
December 22, 2017 – April 20, 2018: Partnership’s review of the draft Phase III WIP planning targets, including consideration of special case requests
Late April/Early May 2018: PSC approval of the final Phase III WIP planning targets with any agreed-to special cases
May 7, 2018: Release of the final Phase III WIP planning targets

## Slide 106: During the 4-Month Review Period
Analyze level of effort to achieve the draft planning targets
Evaluate effects of accounting for growth, Conowingo infill, and climate change on level of effort
Assess the need for exchanges of nitrogen and/or phosphorus loads between a jurisdiction’s major river basins
Assess the need for exchanges of nitrogen for phosphorus or phosphorus for nitrogen within a jurisdiction’s major river basins
Determine if any special cases are needed

## Slide 107: Further Analyses for Consideration
Testing out preliminary development of measurable, local planning goals below the major state-basin level

## Slide 108: Further Analyses for Consideration
Apply the results of the geographic isolation runs to help inform implementation planning and targeting

## Slide 109: Further Analyses for Consideration
1985
2015
Where did the
Nitrogen reductions
come from?
Evaluate potential changes needed to a jurisdiction’s Phase I and Phase II WIP source sector goals

## Slide 110: Support to Jurisdictions During their Reviews
The Partnership Office in Annapolis can support the jurisdictions by helping:
  Test out possible N for P and P for N exchanges
  Test out possible major river basin to basin exchanges
  Test for possible water quality/load reduction impacts on upstream and down tide neighboring jurisdictions
  Think through and help test possible approaches to developing local area planning goals
  Evaluate feasibility of achieving the draft planning targets and what are the opportunities for further reductions by source sector, geography

## Slide 111: Possible Changes Between Now and April 2018
Requests for special conditions
Conducting basin to basin exchanges of N, P, and sediment loads
Conducting significant N for P and P for N exchanges

## Slide 112: What are Special Cases?
Special cases are requests by the jurisdictions for any:
  Changes to their draft Phase III WIP planning targets
  Changes to the methodology used to establish the draft Phase III WIP planning targets

## Slide 113: Who Can Submit a Special Case Request?
Any one of the seven Bay watershed jurisdictions to the CBP Water Quality Goal Implementation Team (WQGIT) Chair and the CBP WQGIT Coordinator

## Slide 114: Notification of Special Case Requests
March 16, 2018
Final deadline for submitting the special case request(s), along with the justification and nutrient and basin exchanges that have multi-jurisdictional impacts, to the Partnership for consideration

## Slide 115: Process for Addressing Special Cases
CBPO staff will work with the jurisdictions to address and identify potential resolutions for special cases during the 4-month review period
For transparency, updates will be provided to the WQGIT during each conference call during the 4-month review period communicating:
  Who has submitted special case requests
  Proposed options for resolving the special case request(s)
PSC will approve any special case requests submitted to the Partnership for review and consideration

## Slide 116: Options for Resolving Special Cases
In the event the PSC cannot reach consensus on the resolution of special case requests, the PSC can either:
  Resolve the issue by a supermajority vote, per the Partnership’s governance procedures, or
  Request that EPA make the final decision

## Slide 117: Today’s Requested Policy Decision
Approval of proposed process for the Partnership’s 4-month review of the draft Phase III WIP planning targets, including addressing special case requests

## Slide 118
Accounting for Growth in the Jurisdictions’ Phase III WIPs
Karl Berger, MWCOG, CBP Land Use Workgroup Chair
and
Peter Claggett, USGS, CBP Land Use Workgroup Coordinator

## Slide 119: Accounting for Growth Equitably Across Jurisdictions
Watershed population is increasing by over 1 million persons/decade
  Population change from 2010 -2025 = 2.0 million persons
Chesapeake Bay Land Change Model (CBLCM) estimates land use and wastewater impacts of future population growth.
  Parameterized uniquely for every state/county/city in the Bay watershed.
  Accounts for uncertainty at sub-county scales.
Partnership agreement on future land use scenarios reflecting a range of planning and conservation efforts.
Developing the WIPs on 2025 land use conditions enable the use of planning and conservation efforts to help “account for growth” for the TMDL.

## Slide 120: Why Account for Growth?
2025 growth projection
Load reductions necessary to meet the 2025 Phase III WIP Planning Target (lock box)

## Slide 121
Chart: Chesapeake Bay Watershed Population Trends
| 1950 | 1960 | 1970 | 1980 | 1990 | 2000 | 2010 | 2020 | 2030 | 2040
Population | 8.3803 | 10.008 | 11.7553 | 12.7383 | 14.2158 | 15.6846 | 17.3462 | 18.7734 | 20.0988 | 21.1434
2010 population = 17.4 million
2025 population = 19.4 million (11.5% increase)

## Slide 122
Chart: Estimated % Change in Animal Units from 2013 through 2025
| DE | MD | NY | PA | VA | WV | CBW
Other | 0.00054342 | -0.0013144 | -0.0079124 | -0.0022325 | -0.017627 | -0.08564 | -0.0088872
Swine | -0.87492 | -0.92039 | 0.056954 | 0.20111 | -0.16262 | -0.96203 | 0.15539
Cattle | -0.298 | -0.36924 | -0.18772 | -0.039886 | -0.048518 | -0.052012 | -0.092137
Poultry | 0.35633 | 0.17466 | -0.064196 | 0.20461 | 0.18542 | -0.034663 | 0.20984
Total | 0.34446 | 0.1251 | -0.15941 | 0.11107 | 0.11664 | -0.039318 | 0.12983

## Slide 123
Chart: Estimated % Change in Sector Acres by Sector from 2013 through 2025
| DC | DE | MD | NY | PA | VA | WV | CBW
Ag | 0 | -0.0050624 | -0.038944 | -0.044952 | -0.031311 | -0.0094357 | -0.013508 | -0.026706
Natural | -0.0039675 | -0.0062923 | -0.0068338 | 0.01166 | -0.0021638 | -0.01419 | -0.0045321 | -0.0057465
Developed | 0.00079193 | 0.036972 | 0.058831 | 0.033929 | 0.072681 | 0.083532 | 0.074895 | 0.069803

## Slide 124: Partnership’s Chesapeake Bay Land Change Model

## Slide 125
Land Change Model Outputs
Impervious surface and turf grass expansion
Forest conversion to development
Farmland conversion to development
Future population on sewer and septic
Rural Residential
57 acres
227 households on sewer
0.25 acre lots
27.8% Impervious
72.2% Turf grass
20-acres farmland loss
37-acres forest loss

## Slide 126: Future Growth Scenarios: 2025
Purpose:
To provide information to state and local partners to account for the effects of land use planning and conservation actions for reducing future pollutant loads in their Phase III WIPs and two-year milestones.
Current Zoning Scenario: 2025 Baseline for Phase III WIPs
Continuation of historic trends constrained by existing local zoning
Includes the best available regional and local data representing current conditions

## Slide 127: Future Growth Scenarios
Conservation Plus Scenario: Package of Planning & Conservation “BMP’s”
  Protect 100-year floodplain and frequently-flooded soils
  Protect riparian zones (35-ft, 100-ft, 300-ft)
  Protect large forest tracts (250+ acres, 1000+ acres) or green infrastructure
  Protect shoreline forests (all contiguous tracts 1000-ft from shoreline)
  Adjusting demand script:
    Increase percent of infill/redevelopment (e.g., 5%, 10%, 15%)
    Increase proportion of urban vs rural growth (e.g., 5%, 10%, 15%)
  Protect Agricultural Districts
  Avoid growth on soils unsuitable for septic systems
  Expand sewer service areas layer (e.g., 1-mile buffer, 2-mile buffer)
  Avoid growth in areas subject to category 3 Hurricane storm surge
  Protect highly productive farms, prime farmlands, farmland of state importance
  Protect state-designated “Healthy watersheds”
  Protect areas subject to marsh migration (e.g., upland buffer around tidal wetlands and National Wildlife refuges)

## Slide 128
Extent of Local Zoning Data
Collected by CBP from local and state agencies, 2013 - 2017

## Slide 129
Residential Infill/Redevelopment
Commercial Infill/Redevelopment
Current Zoning
Scenario
Current Zoning
Scenario

## Slide 130
Increase in Impervious Surfaces
Increase in Turf Grass
Current Zoning
Scenario
Current Zoning
Scenario

## Slide 131: Forest Conversion to Development
Current Zoning
Scenario

## Slide 132: Growth on Sewer and Septic
Current Zoning
Scenario

## Slide 133
Farmland Conversion to Development
Farmland Conversion + Land Retirement
Current Zoning
Scenario
Current Zoning
Scenario

## Slide 134
Jurisdiction | 1985 Baseline | 2013 Progress | Growth in Load to 2025 | Phase III Planning Target
NY | 18.71 | 15.44 | -0.74 | 10.59
PA | 122.41 | 99.28 | 1.66 | 73.18
MD | 83.56 | 55.89 | 1.52 | 45.30
WV | 8.73 | 8.06 | -0.02 | 6.35
DC | 6.48 | 1.75 | 0.00 | 2.43
DE | 6.97 | 6.59 | 0.48 | 4.59
VA | 84.29 | 61.53 | 1.09 | 55.82
Basinwide | 331.15 | 248.54 | 4.00 | 198.25
*Units: millions of pounds
WQGIT & Modeling Workgroup Recommendations: Nitrogen

## Slide 135
Jurisdiction | 1985 Baseline | 2013 Progress | Growth in Load to 2025 | Phase III Planning Target
NY | 1.198 | 0.710 | -0.005 | 0.506
PA | 6.115 | 3.696 | 0.044 | 3.073
MD | 7.419 | 3.919 | -0.015 | 3.604
WV | 0.793 | 0.560 | -0.017 | 0.456
DC | 0.090 | 0.062 | 0.000 | 0.130
DE | 0.225 | 0.115 | 0.007 | 0.120
VA | 13.545 | 6.345 | 0.140 | 6.186
Basinwide | 29.384 | 15.408 | 0.154 | 14.073
*Units: millions of pounds
WQGIT & Modeling Workgroup Recommendations: Phosphorus

## Slide 138: WQGIT Recommendations to the PSC
Use the Partnership’s Land Change Model to establish growth projections, with the opportunity for states (e.g., Maryland) to provide data or alternative modeling approaches in future years, which will be vetted through the Partnership approval process
Use 2025 growth projections based on current zoning as base conditions for the Phase III WIPs
Update the growth projections every 2 years with the best available data to inform the development of the two-year milestones

## Slide 139: Today’s Requested Policy Decisions
Approval of the Water Quality Goal Implementation Team’s recommended use of 2025 projected conditions (based on the current zoning scenario) to account for growth in the development and implementation of the jurisdictions’ Phase III WIPs

## Slide 140: Today’s Requested Policy Decisions
Approval of the Water Quality Goal Implementation Team’s proposed approach to continued Partnership accounting for growth into the future by:
  Updating the Partnership’s projection of future growth every two years
  Factoring these updated future projections into next round of the jurisdictions’ two-year milestones
  Factoring in future (every 4 years) updates to the Partnership’s high resolution land use/cover data across the entire watershed
  Ensuring local partner review of the future growth forecasts with each 2-year update

## Slide 141
Conowingo Dam Infill: How Much, Who, How, and By When
Lee Currey, MDE, CBP Modeling Workgroup Co-Chair

## Slide 142
Almost all of the nutrients are from upstream sources
Much of the nutrients are biologically available to algae when they enter tidal waters
Some of the nutrients are scoured from the bottom sediments behind the dam
Much of these scoured nutrients are not biologically available to algae when they enter tidal waters
Estimated Loads to the Bay with Conowingo Dam and Reservoir at Infill Conditions
Therefore, the determination of nutrient loads to be reduced to account for Conowingo infill must factor in the type of nutrients and the timing of delivery

## Slide 143
Conowingo Effect on Loads at the WIP2 condition

## Slide 144: Estimated Loads to the Bay with Conowingo Dam and Reservoir at Infill Conditions
Additional Phosphorus Loads to be Addressed: 0.26 million pounds
Additional Nitrogen Loads to be Addressed: 6 million pounds

## Slide 145
Who?
How?
When?
Original Options: How to Offset the Additional Loads Due to Conowingo Dam Infill
By 2025
Post-2025 with agreed-upon date
Beyond 2025 – no future date identified
Allocation equity rules used in the Bay TMDL
Assign additional load as local planning goal

## Slide 146
Who?
When?
WQGIT Jurisdictions’ Positions on Who is Responsible for Addressing Conowingo Infill & By When
By 2025
WV, DE & VA
WV & DE
MD
PA, WV, DC, & NY

## Slide 147: Deriving the Draft Phase III Planning Targets: Nitrogen

## Slide 148: Deriving the Draft Phase III Planning Targets: Phosphorus

## Slide 149
Relative Effectiveness with Conowingo in 1990s condition
Relative Effectiveness with Conowingo in current condition
Note changes in Susquehanna relative effectiveness only

## Slide 150
Jurisdiction | Susquehanna Only | Susquehanna + Effective Basins | Susquehanna + MD and VA | Entire Watershed
NY | 0.57 | 0.50 | 0.36 | 0.32
PA | 5.31 | 4.71 | 3.34 | 3.31
MD | 0.12 | 0.78 | 1.97 | 1.76
WV | 0.00 | 0.00 | 0.00 | 0.19
DC | 0.00 | 0.00 | 0.00 | 0.00
DE | 0.00 | 0.00 | 0.00 | 0.32
VA | 0.00 | 0.14 | 1.54 | 1.38
Basinwide | 6.01 | 6.12 | 7.21 | 7.28
Estimated Additional Nitrogen Reductions Required Under the Four Options
*Units: millions of pounds

## Slide 151
Jurisdiction | Susquehanna Only | Susquehanna + Effective Basins | Susquehanna + MD and VA | Entire Watershed
NY | 5.4% | 4.7% | 3.4% | 3.0%
PA | 7.3% | 6.4% | 4.6% | 4.5%
MD | 0.3% | 1.7% | 4.3% | 3.9%
WV | 0.0% | 0.0% | 0.0% | 3.0%
DC | 0.0% | 0.0% | 0.0% | 0.2%
DE | 0.0% | 0.0% | 0.0% | 6.9%
VA | 0.0% | 0.2% | 2.8% | 2.5%
Estimated Additional Nitrogen Reductions Required Under the Four Options

## Slide 152
Jurisdiction | Susquehanna Only | Susquehanna + Effective Basins | Susquehanna + MD and VA | Entire Watershed
NY | 0.027 | 0.020 | 0.013 | 0.012
PA | 0.230 | 0.176 | 0.109 | 0.115
MD | 0.005 | 0.070 | 0.101 | 0.093
WV | 0.000 | 0.000 | 0.000 | 0.013
DC | 0.000 | 0.000 | 0.000 | 0.001
DE | 0.000 | 0.000 | 0.000 | 0.005
VA | 0.000 | 0.000 | 0.162 | 0.150
Basinwide | 0.262 | 0.266 | 0.385 | 0.389
Estimated Additional Phosphorus Reductions Required Under the Four Options
*Units: millions of pounds

## Slide 153
Jurisdiction | Susquehanna Only | Susquehanna + Effective Basins | Susquehanna + MD and VA | Entire Watershed
NY | 5.3% | 4.0% | 2.5% | 2.3%
PA | 7.5% | 5.7% | 3.5% | 3.7%
MD | 0.1% | 1.9% | 2.8% | 2.6%
WV | 0.0% | 0.0% | 0.0% | 2.9%
DC | 0.0% | 0.0% | 0.0% | 0.6%
DE | 0.0% | 0.0% | 0.0% | 4.1%
VA | 0.0% | 0.0% | 2.6% | 2.4%
Estimated Additional Phosphorus Reductions Required Under the Four Options

## Slide 154: WQGIT Recommendations to the PSC
WQGIT-recommended approach recognizes that all jurisdictions have benefited from the Conowingo reservoir and its nutrient and sediment pollution trapping and that there is a less costly approach than assignment of allocations that achieves water quality objectives and does not require reductions by all jurisdictions
Develop a separate implementation plan, which is a Partnership collaboration to address the additional reductions needed as a result of infill
  Address impacts in a way that makes the most scientific and economic sense, and supports those that can reduce pollution more effectively

## Slide 155: WQGIT Recommendations to the PSC
WQGIT-recommended approach recognizes that all jurisdictions have benefited from the Conowingo reservoir and its nutrient and sediment pollution trapping and that there is a less costly approach than assignment of allocations that achieves water quality objectives and does not require reductions by all jurisdictions
Create approach that pools resources
  Pooled resources, which may include funding, technical assistance, advocacy, intellectual property, etc., from all jurisdictions would be managed (both in terms of allocation of funds and verification / tracking of reductions) by a third party under Partnership oversight
  Pooling of resources and implementation would be phased in over time as appropriate

## Slide 156: WQGIT Recommendations to the PSC
Necessary steps to implement proposed approach
  Reach Partnership consensus on the approach
  PSC to send letter to Exelon
  All jurisdictions and other partners develop the plan
  Determine the role of Exelon in plan implementation based on Maryland’s decisions regarding 401 certification
  Finalize plan and determine gaps and contingencies
  Begin plan implementation

## Slide 157: WQGIT Recommendations to the PSC
Necessary steps to implement proposed approach (Continued)
  Evaluate, as is currently done with the milestones, the effectiveness and progress of the plan on an annual basis
  Reevaluate the plan and make any necessary adjustments based on jurisdictional WIP implementation and any other factors that might influence plan success
Need to develop timelines to develop and implement the plan (by 2025?)
  Includes conducting a gap analysis to determine if the plan could be fully implemented by 2025
Conowingo Plan development likely to occur concurrently with Phase III WIP development

## Slide 158: Day Two Requested Policy Decisions
Approval of the WQGIT-proposed approach to account for the additional nutrient loads delivered to the Bay due to the Conowingo infill
Approval of the timeframe by which the jurisdictions have to address the additional nutrient loads

## Slide 159
Factoring in Climate Change into the Jurisdictions’ Phase III WIPs
Mark Bennett, USGS, CBP Climate Resiliency
Workgroup Chair

## Slide 160: PSC-Approved Guiding Principles Phase III WIP Development
Capitalize on “Co-benefits” – maximize BMP selection to increase climate resiliency
Account for and integrate planning and consideration of existing stressors – consider existing stressors in establishing reduction targets or BMP selection
Align with existing climate resilient plans and strategies – document jurisdictions’ action plans and strategies to address climate change
Manage for risk and plan for uncertainty – employ risk management and flexible implementation strategies to achieve and maintain water quality standards
Engage Local Agencies and Leaders – work cooperatively with local partners to provide best available data on local impacts

## Slide 161: PSC-Approved Guiding Principles Phase III WIP Implementation
Reduce vulnerability – use “Climate Smart” principles to site and design BMPs
Build in flexibility and adaptability – allow for adjustments in BMP implementation to consider potential uncertainties and response options
Adaptive manage – allow for changes in BMP selection or WIP implementation over-time

## Slide 162: Accounting for Changing Conditions

## Slide 163: Impact of Changing Conditions on Bay and Watershed Increase Through Time
Based on STAC guidance1, the Partnership is using projections for 2025 that have a high level of confidence
  Selection of projections for sea level rise and precipitation change were based on past records of observed climatic and resultant river flow conditions.
  There is less uncertainty in downscaled temperature projections for 2025.
According to the National Climate Assessment2, impacts associated with precipitation, temperature and sea level are all expected to increase beyond 2025
CBP Scientific and Technical Advisory Committee. 2016. The Development of Climate Projections for Use in Chesapeake Bay Program Assessments. March 2016 Workshop.
4th National Climate Assessment (November 2017)

## Slide 164: Impact of Changing Conditions on Bay and Watershed Increase Through Time
“The Chesapeake Bay Watershed is already experiencing impacts associated with sea level rise (e.g., coastal storm impacts and nuisance flooding) as well as heavy precipitation events1”
“Heavy precipitation events in most parts of the United States have increased in both intensity and frequency since 1901 (high confidence). There are important regional differences in trends, with the largest increases occurring in the northeastern United States (high confidence).2”
CBP Scientific and Technical Advisory Committee. 2016. The Development of Climate Projections for Use in Chesapeake Bay Program Assessments. March 2016 Workshop.
4th National Climate Assessment (November 2017)

## Slide 165
Chart: Year
| 2000 | 2010 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070 | 2080 | 2090 | 2100
0.3m GMSLR low | 0.092957 | 0.19138 | 0.32262 | 0.48666 | 0.58508 | 0.68351 | 0.78193 | 0.84755 | 0.91317 | 0.97878 | 1.0116
0.3m GMSLR high | 0.092957 | 0.32262 | 0.58508 | 0.78193 | 1.0444 | 1.2741 | 1.5365 | 1.7662 | 1.9302 | 2.1271 | 2.3239
0.5m GMSLR low | 0.092957 | 0.257 | 0.38823 | 0.58508 | 0.74912 | 0.94598 | 1.11 | 1.3069 | 1.4709 | 1.635 | 1.7662
0.5m GMSLR high | 0.092957 | 0.35542 | 0.61789 | 0.84755 | 1.11 | 1.4053 | 1.6678 | 1.8974 | 2.0943 | 2.3239 | 2.5208
1.0m GMSLR low | 0.092957 | 0.32262 | 0.51947 | 0.81474 | 1.0772 | 1.4381 | 1.8318 | 2.2583 | 2.6848 | 3.1769 | 3.6363
1.0m GMSLR high | 0.092957 | 0.45385 | 0.78193 | 1.1428 | 1.5365 | 2.0287 | 2.5536 | 3.0785 | 3.6363 | 4.2924 | 4.9814
1.5m GMSLR low | 0.092957 | 0.32262 | 0.55227 | 0.91317 | 1.3069 | 1.8318 | 2.3567 | 3.0129 | 3.6691 | 4.4237 | 5.2439
1.5m GMSLR high | 0.092957 | 0.51947 | 0.91317 | 1.4053 | 1.963 | 2.652 | 3.4066 | 4.2924 | 5.1455 | 6.2281 | 7.3764
2.0m GMSLR low | 0.092957 | 0.48666 | 0.88036 | 1.4381 | 2.0287 | 2.7832 | 3.5706 | 4.4893 | 5.572 | 6.8187 | 8.2622
2.0m GMSLR high | 0.092957 | 0.55227 | 1.0444 | 1.635 | 2.3567 | 3.2426 | 4.2268 | 5.3423 | 6.6546 | 8.0982 | 9.673
2.5m GMSLR low | 0.092957 | 0.32262 | 0.55227 | 1.0116 | 1.6021 | 2.3567 | 3.3082 | 4.4237 | 5.7032 | 7.1468 | 8.7216
2.5m GMSLR high | 0.092957 | 0.58508 | 1.0444 | 1.7334 | 2.5864 | 3.6691 | 4.9158 | 6.3594 | 7.9014 | 9.6402 | 11.8056
Relative Sea Level Rise Scenarios for Annapolis
with Annapolis Monthly Mean Sea Level Data for 1930-2016
The six Global Mean Sea Level (GMSL) scenarios in Sweet et al., 2017, identified by the height in meters in 2100 relative to MSL in 2000, span the range of scientifically plausible sea level rise scenarios. The shaded regions represent a central 80% probability range for each scenario. These curves have been adjusted to depict MSL relative to 1992.
The five scenarios described in Hall et al., 2016 correspond to GMSL of 2.0m, 1.5m, 1.0m, 0.5m, and 0.2m relative to MSL in 1992, and are indicated by thick black lines.
Intermediate Low (0.5m)
Intermediate (1.0m)
Intermediate High (1.5m)
High (2.0m)
Extreme (2.5m)
Low (0.3m)
High Emission Scenario with
Max Contribution from Ice Sheets;
Low Probability, High Consequences
Low Emissions; Requires
Major Carbon Cuts and Removal
Moderate to High Emissions
Graphic by E.T. Petruncio
Relative Sea Level Rise
.17 meter/.6 feet
Sources: Hall et al. (2016) and Sweet et al. (2017)
CBP Climate Resiliency Workgroup recommended 2025 projection: .17 meter/.6 feet
Notes: MSL in 2000 = MSL in 1992 + .092957 ft (based on averages of monthly data)

## Slide 166
Temperature Change
2025/2050 STAC Recommended Projections
1.98° F / 1.1° C Increase in Average Annual Temp
1995-2025
1995-2050
3.5° F / 1.94° C Increase in Average Annual Temp
Source: Kyle Hinson, CRC/CBPO
Notes: Note that the change is in degrees Celsius, it’s kind of a lot

## Slide 167
11
Precipitation Change
2025 STAC Recommended Projection: Trends in 88-years of annual PRISM[1] data
Change in Rainfall Volume 2021-2030 vs. 1991-2000
[1] Parameter-elevation Relationships on Independent Slopes Model
Source: Kyle Hinson, CRC/CBPO
Major Basins | PRISM Trend
Youghiogheny River | 2.1%
Patuxent River Basin | 3.3%
Western Shore | 4.1%
Rappahannock River Basin | 3.2%
York River Basin | 2.6%
Eastern Shore | 2.5%
James River Basin | 2.2%
Potomac River Basin | 2.8%
Susquehanna River Basin | 3.7%
Chesapeake Bay Watershed | 3.1%

## Slide 168
Precipitation Change
4th NCA Future Seasonal Patterns (2070 – 2099)
Projected change (%) in total seasonal precipitation from CMIP5 simulations for 2070–2099. The values are weighted multimodel means and expressed as the percent change relative to the 1976–2005 average. These are results for the higher scenario (RCP8.5).
Source: NOAA NCEI (NCA 2017)

## Slide 169: Accounting for Changing Conditions Cumulative Assessment of Bay Low Dissolved Oxygen Impacts

## Slide 170: Estimated Changes in Watershed and Bay Loads by 2025 Due to Climate Change
Inorganic nutrients are increased with climate change
Organic nutrients are decreased
Inorganic nutrients have a higher effect on dissolved oxygen

## Slide 171
Jurisdiction | 1985 Baseline | 2013 Progress | Climate Change | Phase III Planning Target
NY | 18.710 | 15.440 | 0.400 (3.8%) | 10.594
PA | 122.414 | 99.275 | 4.135 (5.7%) | 73.181
MD | 83.556 | 55.893 | 2.194 (4.8%) | 45.296
WV | 8.727 | 8.065 | 0.236 (3.7%) | 6.347
DC | 6.481 | 1.754 | 0.006 (0.2%) | 2.425
DE | 6.968 | 6.587 | 0.397 (8.7%) | 4.587
VA | 84.295 | 61.530 | 1.722 (3.1%) | 55.822
Basinwide | 331.151 | 248.544 | 9.089 (4.6%) | 198.253
Climate Change Loads: Nitrogen
*Units: millions of pounds

## Slide 172
Jurisdiction | 1985 Baseline | 2013 Progress | Climate Change | Phase III Planning Target
NY | 1.198 | 0.710 | 0.015 (2.9%) | 0.506
PA | 6.115 | 3.696 | 0.143 (4.7%) | 3.073
MD | 7.419 | 3.919 | 0.117 (3.2%) | 3.604
WV | 0.793 | 0.560 | 0.017 (3.7%) | 0.456
DC | 0.090 | 0.062 | 0.001 (0.8%) | 0.130
DE | 0.225 | 0.115 | 0.006 (5.1%) | 0.120
VA | 13.545 | 6.345 | 0.187 (3.0%) | 6.186
Basinwide | 29.384 | 15.408 | 0.485 (3.4%) | 14.073
Climate Change Loads: Phosphorus
*Units: millions of pounds

## Slide 173
Policy Options for Accounting for Climate Change in the Jurisdictions’ Phase III WIPs
Mark Bennett, USGS, CBP Climate Resiliency Workgroup
Co-Chair

## Slide 174: Two Policy Approaches
Numeric
Programmatic
and/or

## Slide 175: Numerical Approach
A quantitative, numerical approach will result in a changed level of effort necessary to meet water quality standards
Account for the increased pollutant loads to each jurisdiction’s portion of the Bay watershed
Accounts for feedbacks to the Bay’s assimilative capacity
This approach would treat the estimated cumulative effect of changed conditions due to climate change similarly to the approach being taken to account for growth
Jurisdictions would develop Phase III WIPs which account for the estimated increased pollutant loads

## Slide 176: Numerical Approach: Pros & Cons
Pros | Cons
Comprehensive, straight-forward approach Demonstrates Partnership’s commitment to Chesapeake Bay Agreement Climate Resiliency Goal Near-term response Implemented in sequence with development of Phase III WIPs | Increased level of effort required to meet water quality standards If implemented in isolation, would not address the anticipated impacts of climate change on BMPs

## Slide 177: Programmatic Approach
An “adaptive management approach” that would be implemented through the two-year milestone process
Would not change a jurisdictions' planning targets
Directs the Partnership to collect and consider new information on the performance of BMPs, including the contribution of seasonal, inter-annual climate variability, and weather extremes.
  Jurisdictions would assess this information and adjust plans, over-time, to better mitigate anticipated changes in loads and impacts on the performance of BMPs.
Would require the inclusion of a narrative strategy in Phase III WIPs, describing a jurisdictions’ programmatic commitments to address climate change.
  A sample “narrative strategy” would be provided to jurisdictions to guide implementation.

## Slide 178: Programmatic Approach: Pros & Cons
Pros | Cons
Adaptively managing for long-term change Allows for use of local expertise and knowledge Provides for learning across jurisdictions about methods and results Allows for flexibility in jurisdictions’ approaches to addressing climate change Provides standard elements to be addressed | If implemented in isolation (w/o numeric approach), delays substantive action to address climate change in the near-term Lack of specific technical understanding to guide implementation Requires additional monitoring and assessment efforts Inconsistency in implementation across jurisdictions

## Slide 179: WQGIT Recommendations to the PSC: Adopt a dual approach to factor climate change into the Phase III WIPs
Adopt a programmatic approach to address climate change
  Include a narrative strategy in the Phase III WIPs that describes the jurisdictions’ current action plans and strategies to address climate change, as well as the jurisdiction-specific nutrient pollutant loadings due to 2025 climate change conditions (derived using the planning targets methodology)
  Incorporate local priorities (e.g., flooding) and actions to address climate change impacts

## Slide 180: WQGIT Recommendations to the PSC: Adopt a dual approach to factor climate change into the Phase III WIPs
Adopt a programmatic approach to address climate change (Continued)
  Document the current understanding of the science and identify the research gaps and needs, and what we hope to learn over time given the current state of uncertainty (e.g., a better understanding of the BMP responses, including new or other emerging BMPs, to climate change conditions)
  Identify a date by which the Partnership will provide additional science and information to help inform implementation efforts to address climate change (early 2021 to inform 2022-2023 milestones?)

## Slide 181: WQGIT Recommendations to the PSC: Adopt a dual approach to factor climate change into the Phase III WIPs
Document and communicate additional nutrient pollutant loads of up to 9 million pounds of nitrogen and 0.5 million pounds of phosphorus due to 2025 climate change conditions
  Continue to understand the nature and effect of climate change impacts in the watershed and estuary to inform management strategies (e.g., WIP/2-year milestones)
  By [insert date], develop recommendations for new and/or refined methods and modeling techniques to better assess projected impacts on watershed loads and estuarine impacts for a range of future scenarios, including the methodology used to develop jurisdiction-specific nutrient pollutant loads due to 2025 climate change conditions

## Slide 182: WQGIT Recommendations to the PSC: Adopt a dual approach to factor climate change into the Phase III WIPs
Document and communicate additional nutrient pollutant loads of up to 9 million pounds of nitrogen and 0.5 million pounds of phosphorus due to 2025 climate change conditions (Continued)
  By [insert date], consider results of updated methods, techniques, and studies and revisit whether to explicitly account for those additional nutrient pollutant loads due to 2025 climate change conditions in the Phase III WIPs and/or 2-year milestones
  Identify a date (post-2025) by which the Partnership will fully address the additional nutrient pollutant loads in a Phase III WIP addendum and/or 2-year milestones

## Slide 183: WQGIT Recommendations to the PSC
Provide the jurisdictions with the flexibility to explicitly account for additional nutrient pollutant loadings due to 2025 climate change impacts in their Phase III WIPs and/or 2-year milestones prior to the Partnership agreed-upon date

## Slide 184: Day Two Requested Policy Decisions
Approval of the WQGIT-proposed dual approach to factor climate change into the Phase III WIPs
Approval of WQGIT recommendation to provide flexibility among jurisdictions and a commitment for CBP programmatic support (e.g., guidance, data, funding, etc.) for implementation of climate change policies that exceed the Partnership approved policies

## Slide 185
Accounting for Changed Conditions in the Jurisdictions’ Phase III WIPs
Teresa Koon, WV DEP, CBP Water Quality Goal
Implementation Team Vice Chair
and
Lee Currey, MDE, CBP Modeling Workgroup Co-Chair

## Slide 186
Jurisdiction | 1985 Baseline | 2013 Progress | Growth in Load to 2025 | Phase III Planning Target
NY | 18.71 | 15.44 | -0.74 | 10.59
PA | 122.41 | 99.28 | 1.66 | 73.18
MD | 83.56 | 55.89 | 1.52 | 45.30
WV | 8.73 | 8.06 | -0.02 | 6.35
DC | 6.48 | 1.75 | 0.00 | 2.43
DE | 6.97 | 6.59 | 0.48 | 4.59
VA | 84.29 | 61.53 | 1.09 | 55.82
Basinwide | 331.15 | 248.54 | 4.00 | 198.25
*Units: millions of pounds
Summary of “All the Numbers”: Nitrogen

## Slide 187
Summary of “All the Numbers”: Phosphorus
*Units: millions of pounds
Jurisdiction | 1985 Baseline | 2013 Progress | Growth in Load to 2025 | Phase III Planning Target
NY | 1.198 | 0.710 | -0.005 | 0.506
PA | 6.115 | 3.696 | 0.044 | 3.073
MD | 7.419 | 3.919 | -0.015 | 3.604
WV | 0.793 | 0.560 | -0.017 | 0.456
DC | 0.090 | 0.062 | 0.000 | 0.130
DE | 0.225 | 0.115 | 0.007 | 0.120
VA | 13.545 | 6.345 | 0.140 | 6.186
Basinwide | 29.384 | 15.408 | 0.154 | 14.073

## Slide 190: Day Two Requested Policy Decisions
Approval of the draft Phase III Planning Targets as the starting point for the 4-month review process
Approval of the approach to account for the additional loads delivered to the Bay due to the Conowingo infill
Approval of how to factor climate change into the Phase III WIPs