## Slide 1
WVWRAM
WV Wetland Rapid Assessment Method
Elizabeth Byers, Senior Wetland Scientist
WVDEP Watershed Assessment Branch
Elizabeth.A.Byers@wv.gov
Notes: Glade Run, 100+ year old beaver wetland, CVNWR; Introduce WVWRAM to DEP leadership

## Slide 2
WVWRAM
WV Wetland Rapid Assessment Method
Background
How it works
Innovations & Refinements
Questions
Notes: Glade Run, 100+ year old beaver wetland, CVNWR; Introduce WVWRAM to DEP leadership

## Slide 3
Catalyst for
developing WVWRAM:
2008 Mitigation rule
for aquatic resources
“no net loss of
wetland function”

## Slide 4: Legal protection of WV wetlands
Clean Water Act 1972
  2008 Mitigation Rule: no net loss of function
WV Water Pollution Control Act 2014
Food Security Act 1985
  Swampbuster
Notes:   NRCS “swampbuster” provision: farmers lose subsidies or do not qualify for federal programs if they destroy wetlands – but they are allowed to continue to farm/drain wetlands that were impacted prior to 1985. Clean Water Act: Corps/EPA Mitigation Rule 2008.

## Slide 5
Financial support from:

## Slide 6: Fish & wildlife, rich biodiversity, productivity
Notes: …now expanded to include: fish and wildlife, extensive food chain and rich biodiversity
  (Cranesville swamp, Black Bear, Insect, Canada Lily, common yellowthroat)

## Slide 7: Fish & wildlife, rich biodiversity, productivity
Chart: Area
| Wetland | Upland
 | 156 | 23882
Chart: Biodiversity
| Wetland | Upland
 | 23 | 77
Chart: Rare Species
| Wetland | Upland
 | 44 | 56
0.6%
23%
44%
Notes: …now expanded to include: fish and wildlife, extensive food chain and rich biodiversity
  (Cranesville swamp, Black Bear, Insect, Canada Lily, common yellowthroat)

## Slide 8: kidneys of the landscape
Notes: kidneys of the landscape
  cleanse polluted waters: receive of water and waste from both natural and human sources
Naturally-occurring bacteria in wetlands convert polluting nitrates into harmless nitrogen gas, filtering and purifying water for areas downstream.

## Slide 9: stabilize water supplies
Pinus rigida - Picea rubens / Viburnum nudum var. cassinoides / Sphagnum spp. Woodland (G1G2)
Notes: stabilize water supplies, thus mitigate both floods and drought, recharge groundwater aquifers
Large headwater wetlands in the Allegheny Mountains and Meadow River provide important flood protection services to the state.
Pitch pine – heath peat woodland S1 / G1G2 : Northern-affiliated Swamps, Allegheny Front and the Catskills of NY.

## Slide 10: protect shorelines and banks from erosion
Notes: Justicia meadow, Plot CAPR.4 Denmar, Greenbrier River
(Jim Vanderhorst photo)

## Slide 11
2015-16 Develop tool for functional assessment of wetlands
Notes: Building on best available science.

## Slide 12
Built on the best available existing science
Notes: Obstacle! Lack of resources and personnel
  Build on shoulders of giants
  Use only well-vetted approaches and metrics that have survived rigorous testing for repeatability, sensitivity, and are clearly linked to function and are RAPID
  Where pockets of local expertise exist, seize them (NRCS & soils metrics)
Draw heavily on OR and WA for methods, plus CA and NatureServe for the habitat function. Extensive validation of metrics, sensitivity analysis, and repeatability tests done by literally hundreds of wetland scientists. Ohio for stressors, Minnesota for Rapid FQA, Montana for wildlife habitat, WI for GIS-RAM inspiration, plus many other states. WV benefits from the outstanding work done by many of the people in this room.

## Slide 13
…DEP looked only at tested, validated methods & metrics
Notes: I also searched the recent literature for any studies linking wetland functions to measurable wetland characteristics, and picked up a few more guidelines. Lots of reading in those first few months of the project!

## Slide 14
2017-18 Field-testing:
69 stakeholders from 22 organizations
Notes: Fine-tuning metrics based on stakeholder input; building familiarity and ownership of WVWRAM. Industry, agencies, consultants, NGOs.

## Slide 15
2019 Training:
112 stakeholders from 40 organizations
Notes: Training

## Slide 16
2020 Monitoring:
initiate probabilistic statewide program
Notes: Training

## Slide 17
2020
public notice and moving toward agency adoption
Notes: Obstacle! How to finish the last mile and officially adopt the new methods?
  Going through the public noticing and changing the legislative rule requires buy-in from IRT, NRCS Technical Committee, and support from agencies
Presentations to stakeholders, lots of peer review, being responsive to their concerns – we need their help to get the policies adopted, and/or not to have them shot down
  Not just agencies. Need industry, environmental consultants (who talk to industry), conservation organizations, anyone who might shoot it down in a public notice.

## Slide 18
WVWRAM
WV Wetland Rapid Assessment Method
Background
How it works
Innovations & Refinements
Questions
Notes: Glade Run, 100+ year old beaver wetland, CVNWR; Introduce WVWRAM to DEP leadership

## Slide 19
Ecological integrity & wildlife habitat
Flood attenuation
Water quality: sediment, nutrients, pollutants
3 composite functions

## Slide 20
75 metrics in 9 categories
 | Intrinsic Potential | Landscape Opportunity | Value to Society
Water Quality | vegetation, soil, hydrology | 50 m buffer, contributing watershed | public use, planning
Flood Attenuation | vegetation, soil, hydrology | 50 m buffer, contributing watershed | economic risk
Habitat/ Ecological Integrity | vegetation, soil, hydrology | perimeter, 300 m / 1 km buffer, contrib. watershed | investment, public use, access
Regulatory score: 65 metrics
Notes:   Full score has 75 metrics in 9 categories

## Slide 21
62 statewide GIS datasets
Biodiversity
Ecosystems
Elevation
Geology
Hydrology
Imagery
Infrastructure
Jurisdiction
Landcover
Landform
Soils
Stressors
Notes:   Amazing to me how much geospatial data is available, putting meaningful GIS-RAM within reach.

## Slide 22
Roll-up of metrics into stakeholder-requested scores:
Regulatory score: physical, chemical & biological
Full function (all metrics)
State lands acquisition
Condition assessment

## Slide 23: GIS plus rapid field assessment: the best of landscape-level assessment + metrics that must be obtained in the field
= WVWRAM
score
+

## Slide 24
Rapid Field Assessment
Notes: Sampling soil at Little River wetland (Jared Beard and Pam Byrne): photo by Elizabeth Byers; Sampling aquatic bed vegetation at Red Creek Plains (Danielle Elliott): photo by Elizabeth Byers; Measuring bankfull width, Jefferson County (Elizabeth Byers, John Burkhart); Sampling soil at Sleepy Creek (Elizabeth Byers, Nick Murray, John Burkhart).

## Slide 25
Vegetation, Soils, Hydrology, Buffer, Stressors
Level of effort: 2 technicians x half-day
Skill level: wetland delineation
plus 2-day training
Rapid Field Assessment
Notes: Sampling soil at Little River wetland (Jared Beard and Pam Byrne): photo by Elizabeth Byers; Sampling aquatic bed vegetation at Red Creek Plains (Danielle Elliott): photo by Elizabeth Byers; Measuring bankfull width, Jefferson County (Elizabeth Byers, John Burkhart); Sampling soil at Sleepy Creek (Elizabeth Byers, Nick Murray, John Burkhart).

## Slide 26
WVWRAM Work Flow
Desktop scenario planning
(if regulatory, then…)
Notes:   Flowchart of WVWRAM including GIS and Rapid Field Assessment

## Slide 27
Chart: Preliminary GIS Score vs. Final Score

## Slide 28
WVWRAM allows scenario planning
WVDEP Watershed Assessment Branch
GIS-based desktop planning supported
Predict mitigation costs of different sites or corridors
Compare potential mitigation credits at different sites prior to land acquisition
Compare conservation outcomes within/between watersheds
Notes: Glade Run, 100+ year old beaver wetland, CVNWR; Getting close to roll-out; share some of the cool stuff we learned.

## Slide 29
WVWRAM Manuals

## Slide 30
WVWRAM Database

## Slide 31: GIS Tool: https://mapwv.gov/wetlands/

## Slide 32: GIS Tool: https://mapwv.gov/wetlands/

## Slide 33: GIS Tool: https://mapwv.gov/wetlands/

## Slide 34: GIS Tool: https://mapwv.gov/wetlands/

## Slide 36
Chart: Regulatory Wetland Function Score
PEM mean = 0.46
PFO mean = 0.65
Preliminary Regulatory Scores (GIS only)
Median score = 0.56
Notes:   98% of WV wetlands have a WVWRAM score between 0 and 1.

## Slide 37
Deter impacts to high-functioning wetlands
Chart: Preliminary Regulatory Scores (GIS only) for 10,416 vegetated wetlands
2% of wetlands are of special conservation concern (“exemplary” with documented global biodiversity significance) and score above 1.0; these get a strong deterrent multiplier of 3 to the score when entered into the SWVM
Notes:   Special conservation concern: 2% of WV’s wetlands contain documented, irreplaceable biodiversity of global significance. These wetlands provide critical habitat to vulnerable species or natural communities with fewer than 80 occurrences worldwide. No amount of mitigation can replace their functions in West Virginia. Rather than taking them off the table entirely, an economic deterrent (3 times the normal mitigation) is placed on them. Rarely will projects encounter these wetlands, and when they do, they should avoid them.

## Slide 38
Preliminary GIS Score for every mapped wetland in WV
WVDEP GIS Viewer

## Slide 39
WVWRAM
WV Wetland Rapid Assessment Method
Background
How it works
Innovations & Refinements
Questions
Notes: Glade Run, 100+ year old beaver wetland, CVNWR; Introduce WVWRAM to DEP leadership

## Slide 40
Wetlands of
Special Conservation Concern
based on Site Biodiversity Rank
Documented by WVDNR
Natural Heritage Data
Innovation #1
Link natural heritage
data to GIS tool
Notes: Override is applied to wetlands with documented and significant biodiversity. B1-B3: Global (100-200); B4-B5: state (30-50); B6: county (5).

## Slide 41: Python-based automation
Innovation #2
Notes: Updated mapping or layers – no problem! Yibing Han, python programmer at WV GIS Tech Center.

## Slide 42: Floristic Quality Assessment
Rapid
Mean abundance-weighted CoC using 50/20 Rule vs. Full Floristics
Innovation #3
Notes: Pioneered by Minnesota & Pennsylvania. North Carolina now also developing Rapid FQA.

## Slide 43: Level 2: Field Assessment
Refinement #1
Field mapping of entire
wetland with NWI attributes
PFO4Bag = palustrine forested needle-leaved evergreen swamp on seasonally saturated acidic organic soil
Notes: Whitmeadow Run on Cheat Mountain; field mapping of full NWI attributes

## Slide 44
Depth of organic material
Calcareous soil
Hydrologic regime
Compaction / Stressors
Refinement #2
Soils & Wetland Function

## Slide 45
Make it easy to use
Type “WVWRAM” into your search engine

## Slide 46
Questions?
Elizabeth.A.Byers@wv.gov
WVWRAM: robust, repeatable, rapid functional assessment for regulation, restoration, and conservation

## Slide 47
Extra slides to help with answering questions

## Slide 48
WVWRAM
scenarios
WVDEP Watershed Assessment Branch
Standard impact to emergent
Standard impact to forested
Special conservation concern

## Slide 49: Scenario 1: standard impact emergent WV Regional Tech Park example
0.1 acre of emergent
WVWRAM Score = 0.44
Required replacement units =
0.1 acre x 0.44 x 2 = 0.088 credits

## Slide 50: Scenario 2: impact to part of forested wetland

## Slide 51: Scenario 2: impact to part of forested wetland
0.1 acre of larger forested wetland
WVWRAM Score = 0.71
Required replacement units =
0.1 acre x 0.71 x 3 = 0.213 credits

## Slide 52: Scenario 3: Special Concern
0.1 acre of exemplary forested wetland
WVWRAM Score = 1.46
Required replacement units =
0.1 acre x 1.46 x 3 x 3 = 1.31 credits

## Slide 53: Scenario 3: Special Concern
WVWRAM Scores
Two “bins”: 98% restorable (score 0-1)
2% exemplary (score >1)

## Slide 54
WVWRAM credits/debits are cost-neutral
WVDEP Watershed Assessment Branch
Average amount of mitigation required statewide will not change due to WVWRAM
However, individual projects will see changes
Low-functioning wetlands will require less mitigation than under the current system
High-functioning wetlands will require more mitigation than under the current system
Notes: Glade Run, 100+ year old beaver wetland, CVNWR; Getting close to roll-out; share some of the cool stuff we learned.

## Slide 55
Least burdensome way to comply with the 2008 mitigation rule
WVDEP Watershed Assessment Branch
WV is currently in compliance with the mitigation rule for streams, but NOT for wetlands
WVWRAM was developed at the request of the Inter-Agency Review Team.
WVWRAM as part of SWVM offers simple & streamlined permitting, predictable costs
Notes: Glade Run, 100+ year old beaver wetland, CVNWR; Getting close to roll-out; share some of the cool stuff we learned.

## Slide 56
WVWRAM will be required when:
WVDEP Watershed Assessment Branch
there will be permanent impacts to wetlands
there will be temporary impacts to wetlands AND a type conversion will occur (e.g. forested to emergent)
Section 404/401 permitting is triggered
WVWRAM score will be an input to SWVM
Notes: Glade Run, 100+ year old beaver wetland, CVNWR; Getting close to roll-out; share some of the cool stuff we learned.

## Slide 57
Representative Sampling
WVDEP Watershed Assessment Branch
Wetlands that are < 1 acre in size AND with preliminary GIS scores varying < 10% from one another may be considered as a comparable assessment group.
Field assessments of a randomly selected 10% of these wetlands will be accepted as representative of the whole group.

## Slide 58
Year-round Assessment
WVDEP Watershed Assessment Branch
WVWRAM is designed to produce robust, repeatable results during the growing season. Assessors are strongly encouraged to perform the assessment during the months of May-September (June-September for elevations above 3000 feet).
Outside this period, the maximum score for the Rapid Floristic Quality metric is assigned to debits, and the minimum score for Rapid Floristic Quality is assigned to credits.

## Slide 59
WVWRAM and wetland conversion
WVDEP Watershed Assessment Branch
WVWRAM may be used in the future to determine mitigation requirements for a project when:
“conversion” of resource type occurs, for example when a forested wetland is converted to an emergent wetland.
Notes: Glade Run, 100+ year old beaver wetland, CVNWR; Getting close to roll-out; share some of the cool stuff we learned.

## Slide 60
WVWRAM and banking/ILF
WVDEP Watershed Assessment Branch
WVWRAM will become part of the baseline and monitoring requirements for credit release
WVWRAM will be an input to SWVM calculation of credits for restoration, enhancement, and preservation

## Slide 61
Predicting WVWRAM Scores
WVDEP Watershed Assessment Branch
Prep work (checking nearby wetland scores or running desktop scenarios) before you go to the field will allow you to ballpark estimate the WVWRAM score for impatient clients while still in the field.

## Slide 62
SWVM Proposal: Wetlands Parts I-II

## Slide 63
SWVM Proposal: Wetlands Part III

## Slide 64
SWVM Proposal: Wetlands Parts IV-V

## Slide 65
Restoration Planting Community Prediction Tool: West Virginia
© 2013 West Virginia Division of Natural Resources (WVDNR) and the Carolina Vegetation Survey (CVS)
Part of research efforts at the University of North Carolina at Chapel Hill. Programming by Michael T. Lee. Plot data from the WVDNR Natural Heritage Database.
Adaptation of the software tool to West Virginia was made possible by support from The Nature Conservancy and the West Virginia Department of Environmental Protection.
Enter site data
and find similar
community targets

## Slide 66
WV Wetlands
National Wetlands Inventory (1980’s)
66,200 acres mapped
~100,000 acres probably exist
~500,000 acres historically